## Slide 1: Teaching Advanced Electronics
Jim Halderman
Curt Ward

## Slide 2: Introductions
Jim Halderman
Author and former automotive instructor
Curt Ward
Automotive Instructor
Joliet Junior College
Co-author of Light Vehicle Diesel Engines

## Slide 3: Topics to be Discussed
Where we are today
Tools
High Voltage
Advanced Driver Assistance Systems
Telematics
Autonomous vehicles

## Slide 4: ASE Comfort Tasks Today
power window, power seats, power locks, remote start, sun roof, remote keyless entry

## Slide 5: Safety Systems Specified by ASE
Horn, airbags, seat belt pretensioners, wipers, washers, speed control, heads-up display, park assist, and back-up camera

## Slide 6: More Tasks Specified Today
Security/anti-theft systems and related circuits (theft deterrent, door locks, remote keyless entry, remote start, and starter/fuel disable)

## Slide 7: ASE High Voltage Tasks
Identify safety precautions for high voltage systems on electric, hybrid, hybrid-electric, and diesel vehicles.
Identify hybrid vehicle auxiliary (12v) battery service, repair, and test procedures.

## Slide 8: Teaching Today
Test light
DMM

## Slide 9: DMM
Voltage Drop
Resistance – Only uses when spec is above 1 ohm
Current – within limitations of the meter

## Slide 10: Teaching Today?
Scope?
Infrared Camera?

## Slide 11: What we are currently teaching

## Slide 12: What the student needs to understand

## Slide 13: Historical Look at Ohms Law
Electromotive Force = Voltage
Intensity = Amperage = Current
Resistance = Resistance = Ohms
Old model was:
Volts = water pressure in a hose
Current = the flow of the water
Resistance = opposes flow of the water
(How does the water get back in the hose? Complete circuit?)

## Slide 14: Basic Electricity Can be Confusing!
The old model of water didn’t make it
90% of techs can’t do a voltage drop test, why?
DC is often misunderstood at the ground side
AC is not taught
We can’t see electricity!!

## Slide 15: Print out a wiring diagram
Color your power circuits with a light blue highlighter or any color you like
Keep it simple
Draw your own diagram if the print out is too complicated
Color your ground circuits with a yellow (another color?) highlighter
Some techs are red/green color blind

## Slide 16: What Special Tools Might Need to be Purchased?
Are there new tasks?
How can we keep from damaging the vehicle?
How do we keep the student/technician safe?

## Slide 17: High Voltage Orange Cables

## Slide 18: Service Disconnect
Typical Toyota (cover removed)
Typical Ford

## Slide 19: “Blue” Cables

## Slide 20: 1000 Volt Rated Gloves

## Slide 21: High Current Clamp
200/2000A Rating
Hybrid and EV Electric Motor Current
Relative Compression Testing
Starter and Alternator

## Slide 22: Relative Compression Test

## Slide 23: Parasitic Draw Using a Clamp-on Meter

## Slide 24: Low Ohms Cannot be Measured Using a DMM
Even the best meters are not capable of measuring resistance less than one Ohm
Check the meter by selecting Ohms
Touch the two test leads together.

## Slide 25: Milli-Ohm Meter
Electric Motor Winding (balance) Testing

## Slide 26: Meg-Ohm Meter
Loss of Isolation Testing

## Slide 27: DC Loss of Isolation

## Slide 28: High Speed/ Capacity Scope

## Slide 29: Upgraded Scan Tool

## Slide 30: J2534 Device – Module Reprogramming

## Slide 31: Why are we going to higher volts?
With more voltage (strength) you can use less Amps and get the same amount of work done (watts)
Less amps = smaller wires, less weight, less heat
42 Volt Lithium Battery

## Slide 32: High Voltage Battery
Prius
Tesla

## Slide 33: Tesla Super Chargers

## Slide 34: Making Sure Both Contactors Opened

## Slide 35: Improper Test Procedure
The good news: Nobody died!
The bad news: The car would not start and a loss of isolation code was set.
The expensive news: High voltage cables had to be replaced.

## Slide 36: Corrosion on the High Voltage Connections

## Slide 37: Electric Motors

## Slide 38: Electric Motors
3 Phase
Brushless
AC
  Synchronous
  Asynchronous

## Slide 39: Why is AC Important?
Because we can lower and raise the voltage with much less heat than DC
Smaller Wires
Constantly changing amplitude
Periodically changes direction
Flows in cycles

## Slide 40: AC Loss of Isolation

## Slide 41: Inverters and Converters

## Slide 42: Other High Voltage Components

## Slide 43: ADAS

## Slide 44: 2 Levels of ADAS
System Warnings (Base Models)
Visual
Audio
Haptic
System Intervention (Higher Trim Levels)
Maintains Vehicle Speed
Automatically Brakes and Accelerates
Gently Turns Vehicle
Keeps Vehicle Centered in Lane

## Slide 45: ADAS Acronym Decoder
ACC: Adaptive Cruise Control
DSRC: Dedicated Short Range Communication
EPS: Electronic Power Steering
ESR: Electronically Scanning Radar
HMI: Human Machine Interface
HMW: Headway Monitoring and Warning
IFV: Intelligent Forward View
LDW: Lane Departure Warning
LiDAR: Light Imaging Detection and Ranging
LRR: Long Range Radar
MRR: Medium Range Radar
PCW: Pedestrian Collision Warning
Radar: Radio Detection and Ranging
SAE: Society of Automotive Engineers
SLI: Speed Limit Indication
TSR: Traffic Signal Recognition
V2I: Vehicle to Infrastructure
V2V: Vehicle to Vehicle

## Slide 46: Radar (Adaptive) Cruise Control

## Slide 47: Blind Spot Warning
Very commonly found on most newer vehicles.

## Slide 48: Lane Departure Warning
Just a warning if too close to lane marking line.
center line and the right lane line is often called the “fog line”

## Slide 49: Lane Keep Assist
More than a warning.
This system uses the electric power steering (EPS) to steer the vehicle back into the lane
Can be intrusive

## Slide 50: Automatic Braking
Gives an audible and a visual warning.

## Slide 51: Cross Traffic Alert
Uses short range radar

## Slide 52: Parking Assist Systems

## Slide 53: Night Vision Infrared Camera

## Slide 54: Multiple sensors

## Slide 55: Most Current ADAS Systems Technology

## Slide 56: Haptic Sensor
Uses a vibration in the seat or steering wheel to notify the driver. Uses DC motor with a attached weight that is out-of-balance to create the vibration.

## Slide 57: Lidar Sensor
Also called “laser radar”
Uses lasers to “paint” a picture of the surrounding area
Use TBD!

## Slide 58: Cameras
Backup –Required in all 2018+ vehicle.

## Slide 59: Cameras
Used to replace the human eye
Able to recognize objects better than radar
Affected by rain, snow, mud, ice,
Can’t see in the dark or when looking directly into the sun
Static and Dynamic calibration procedures

## Slide 60: Camera Service
Very few replaceable components
Mounting bracket position is critical
Aftermarket replacement windshield glass quality a concern
Windshield chip repair may affect operation
Special cleaning procedures

## Slide 61: Radar
Short range and long range
Long range extends to over two football fields ahead

## Slide 62: Radar
25 GHz Ultra Wide Band Radar
24 GHz Narrow Band Radar
77 GHz Multi Mode Radar
Detection Distance dependent on angle
  < 100 ft. - angle 30 degrees
  100-325 ft. – angle 20 degrees
  325-650 ft. – angle 12 degrees

## Slide 63: Case Study
Message on Dash
Sensor behind Grill Emblem

## Slide 64: Steering Torque Sensor

## Slide 65: Tech Tip
Rear radar unit communication concern
Bumper Cover Cool to Touch on Left Side
Bumper Cover Warm to Touch on Right Side
Right Side Operating Normally – Left Side Inoperative

## Slide 66: Ultrasonic Technology
Ultrasonic sound waves used to detect objects near the vehicle
Early vehicles only had rear sensors
Current systems can detect both forward and reverse
System can detect both distance and direction of the object

## Slide 67: Module Electrical Diagnosis
Does it have power?
Does it have ground?
Is communication present?
Replace Module and
Program Module

## Slide 68: Ultrasonic Sensors
Short range
Used for parking assist systems

## Slide 69: Ultrasonic Sensor Diagnosis using Pico Scope

## Slide 70: Sensor (Camera and Radar) Calibration

## Slide 71: Static Calibration
Physical measurements on flat surfaces to place targets
Scan tool procedures to aim radar and cameras
Some systems static calibration only
Most systems require static and dynamic calibration

## Slide 72: Dynamic Calibration
System in calibration mode using scan tool
Radar and/or Cameras
Specific types of driving
  Minimum speed
  Specific items along route
  Drive time depends on accuracy of static calibration
  May be difficult to complete in urban areas

## Slide 73: Network Communication
CAN Bus
Flex Ray
  Increased fault tolerance for safety systems
  More bandwidth
  10 megabits per second per channel
Isolated Networks for Cyber Security
  Firewall against malicious software and commands
Ethernet for Infotainment

## Slide 74: Vehicle-to-Vehicle Communication
  300 M (980 ft.) Range
  5.9 GHz frequency and 75 MHz bandwidth to transmit
  Alerts: Hard Braking, Disabled Vehicles, Slippery Roads

## Slide 75: Vehicle-to-Infrastructure
V2X
Can include 5G and used before cell phone use.

## Slide 76: Putting it all Together

## Slide 77: Telematics

## Slide 78: Telematics Companies

## Slide 79: Dongle Issues
Data Corruption
Security Issues
  Hackers

## Slide 80: Six Levels of Automation

## Slide 81: What is the Future?
The major change to the automotive industry will be what is being referred to as:
ACES Vehicles
Autonomous Connected Electrified Shared

## Slide 82: Peek Preview 6th edition coming out in early January, 2019

## Slide 83: Summary
ASE Tasks are changing
Plan Budgets to include new technology
Stay Safe – High Voltage is here to stay
ADAS systems are widely available for class now
Try to experience level 2-3 autonomous vehicles if possible. (It is really awesome!)
Until that time:
“Keep your hands on the wheel and your eyes on the road”

## Slide 84: Contact Information
Jim Halderman- jim@jameshalderman.com
Curt Ward- curt@curtward.net

## Slide 85: May You Enjoy Safe Travels
We hope to see you at a conference in the future
Thanks for attending
Don’t forget to thank our hosts