Exhaust System Backpressure Test

Meets NATEF Task:  (A8-D-11)  P-2  Perform exhaust system back-pressure test; determine necessary action.

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

A clogged or partially restricted exhaust greatly affects engine performance.  Lack of power is a common symptom of a partially restricted exhaust system.  In severe cases, the engine may start/stall due to exhaust system restriction.

_____  1.  Check service information for the specified maximum backpressure. ______________

__________________________________________________________________

_____  2.  Remove the oxygen sensor from the

exhaust manifold and install tool to

measure exhaust back pressure.

NOTE:  This tool can be made from an 18 mm fitting and a vacuum hose nipple.

_____  3.  Connect a vacuum/pressure gauge to the exhaust back pressure tool.  Start the engine

and run at idle and observe exhaust back pressure.

______ psi back pressure (maximum allowable back pressure at idle

is 1.25 psi.)

OK _____	NOT OK _____

_____  4.  Operate the engine at a constant speed of 2500 RPM and observe the exhaust back

pressure.

______ psi back pressure (Maximum allowable back pressure at 2500

RPM is 2.5 psi.)

OK _____	NOT OK _____

_____  5.  Based on the results of the backpressure test, what is the necessary action?

_________________________________________________________________