Fluid Leakage Diagnosis

Meets NATEF Task:  (A8-A-4)  Inspect engine assembly for fuel, oil, coolant, and other leaks; determine necessary action. (P-2)

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

Engine oil is usually amber in color when new, but quickly becomes darker and often black when used in an engine.  Before trying to repair an engine oil leak, make sure that the leak is actually engine oil and not some other fluid such as the following:

- red – automatic transmission fluid (also used in some power steering units)

- green – antifreeze coolant

- orange – antifreeze coolant

- blue – antifreeze coolant or windshield washer fluid

- yellow – windshield washer fluid

- clear – condensation from the air-conditioning system (normal)

_____  1.  Carefully inspect the areas where fluid is likely to leak, including:

valve covers	                	OK _____     NOT OK _____

intake manifold area        	OK _____     NOT OK _____

oil pressure-sending unit 	OK _____     NOT OK _____

Radiator/hoses                        OK _____     NOT OK _____

Transmission/lines                  OK _____     NOT OK _____

_____  2.  Safely hoist the vehicle and carefully inspect the underneath of the vehicle.

_____  3.  Where is the highest, most forward area of the leak? (describe)  ________________

___________________________________________________________________

_____  4.  If the exact location cannot be located, lower the vehicle and add fluorescent dye to

the unit believed to be leaking oil.  Drive the vehicle for 10 to 15 minutes and hoist the

vehicle.

_____  5.  Using black light, locate the area of the leak by looking for the yellow/green areas

highlighted by the dye.  Describe the leak location:

____________________________________________________________

_____  6.  Based on the inspection for oil leaks, what is the necessary action? _______________

_____________________________________________________________________