Engine Exhaust and Sound Diagnosis

Meets NATEF Task: (A8-A-4) Diagnose abnormal exhaust color, odor, and sound; determine necessary action. (P-2)

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

_____  1.  Start the engine and observe the exhaust.

____  OK (no visible exhaust smoke)

____  Light amount of visible steam (usually normal)

____  Heavy white steam or smoke (possible coolant leak into the combustion

chamber)

____  Black exhaust smoke (usually caused by a rich air-fuel mixture)

____  Gray exhaust for a second or two, then no exhaust smoke (normal)

____  Blue exhaust smoke at start-up, then normal exhaust (usually caused by

defective valve stem seals)

____  Blue exhaust smoke all the time (engine is using oil)

____  Other (describe) _____________________________________________

_____  2.  Exhaust odor (exhaust does have some smell due to

the various hydrocarbons used in the fuel).

____  Normal

____  Abnormal (if abnormal describe)

_____________________________

_____  3.  Exhaust sound

____  Normal

____  Hissing (check for exhaust leak) and

describe the location __________________________________________

____  Loud (determine the reason and the necessary action to correct the fault ___

_____________________________________________________________

____  Other (describe) _______________________________________________

_____  4.  Based on the analysis above, check service information to determine the steps needed

to correct the concerns.  _________________________________________________

_________________________________________________________________

_____  5.  What is the necessary action? _____________________________________________

_________________________________________________________________