### Compression Testing

Meets NATEF Task:  (A8-A-7)  Perform cylinder cranking and running compression tests; determine necessary action. (P-1)

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

_____  1.  Remove all spark plugs (be certain to label the spark plug wires) and disable the

ignition system to avoid possible ignition coil damage.

_____  2.  Block open the throttle and choke (if equipped).

_____  3.  Crank the engine at least 4 “puffs” (compression strokes) while observing the gauge.

NOTE:  For accurate test results, the engine should be at normal operating

temperature.

RESULTS:  1st puff / final reading      	1st puff / final reading

1.  ___________/__________  		5.  ___________/__________

2.  ___________/__________  		6.  ___________/__________

3.  ___________/__________  		7.  ___________/__________

4.  ___________/__________  		8.  ___________/__________

NOTE:  The 1st "puff" should be more than one-half of the pressure of the final

puff.  If the 1st puff is low, worn piston rings are likely – repeat the test.

_____  4.  Reinstall all spark plugs except one.  Perform a running compression test at idle and at

2000 RPM for each cylinder:

Idle                           		2000 RPM

1. ________________________     1.  ________________________

2. ________________________     2.  ________________________

3.  _______________________      3.  ________________________

4.  _______________________      4.  ________________________

5.  _______________________      5.  ________________________

6.  _______________________      6.  ________________________

- _______________________     7.  ________________________

- _______________________     8.  ________________________

OK_____	NOT OK_____

_____  5.  Based on the test results, what is the necessary action? _________________________

_____________________________________________________________________