Ignition Inspection and Testing

Meets NATEF Task:  (A8-C-1) P-2 Inspect and test ignition primary and secondary circuit wiring and solid state components; test ignition coil(s); perform necessary action.

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

_____  1.  Check service information for the specifications and testing procedures for the

secondary ignition wiring.

__________________________________________________________________

_____  2.  Carefully check the spark plug wire for damage or burned areas that could indicate a

break in the insulation.

OK _____     NOT OK _____

_____  3.  Set the digital multimeter to read ohms (().

_____  4.  List the length in feet and the resistance values in

ohms for each spark plug wire according to the

cylinder number:

Length (feet)        Ohms

1. ___________    __________

2. ___________    __________

3. ___________    __________

4. ___________    __________

5. ___________    __________

6. ___________    __________

7. ___________    __________

8. ___________    __________

Coil wire: (if equipped)

___________    __________

_____  5.  Results - Original equipment radio suppression wires should test 10,000 ohms (10K()

or less per foot of length.

OK _____	NOT OK _____

_____  6.  Based on the inspection and test(s), what is the necessary action? ________________

_________________________________________________________________