TP Sensor Voltmeter Test

Meets NATEF Task:  (A8-B-7) P-2   Inspect and test sensors, actuators, and circuits using a graphing multimeter (GMM)/digital storage oscilloscope (DSO); perform necessary action.

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

_____  1.  Check service information for the location, specifications for the throttle position (TP)

sensor.

_____  2.  Carefully back probe the wires at the connector to gain access to the 5-volt reference,

signal, and signal return (ground) terminal.

_____  3.  With the ignition on, engine off (KOEO), set the digital multimeter (DMM) to DC

volts and attach the black meter lead to a good clean engine ground.

_____  4.  Measure the reference voltage (should be close to 5 volts) = ________.

_____  5.  Measure the sensor signal voltage at idle ____________,

specification = ___________________.

_____  6.  Measure the TP sensor at wide-open throttle (W.O.T.) = ___________________ volts

(should be about 4.5 volts).

_____  7.  Measure the voltage (voltage drop) between the signal return at the TP sensor and a

good clean engine ground.

_____ volts (should be less than 0.2 volts)

_____  8.  Based on the test results, what is the necessary

action?

___________________________________

___________________________________

___________________________________

___________________________________