Throttle Position Sensor Resistance Test

Meets NATEF Task:  (A8-B-7) P-2  Inspect and test sensors, actuators, and circuits using a graphing multimeter (GMM)/digital storage oscilloscope (DSO); perform necessary action.

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

_____  1.  Check service information for the specified testing procedures and resistance values of

the throttle position sensor.

__________________________________________________________________

__________________________________________________________________

_____  2.  After disconnecting the electrical connectors, measure the resistance of the TP sensor

using a digital multimeter (DMM) set to read ohms (Ω).

a.  Measure the resistance between the terminals for the 5-volt reference and the

signal resistance (ground) terminal.

_________ (should be about 1000 ohms (0.8 to 1.1 KΩ)

____ OK    ____ NOT OK

b.  Measure the resistance between the 5-volt reference terminal and the signal

wire.

_____ ohms

c.  Depress the accelerator and observe the meter.  Does the resistance increase or

decrease?  Why?

____________   ______________________________________________

____________________________________________________________

_____  3.  Based on the tests performed, what is the necessary action? _____________________

_____________________________

_____________________________

_____________________________