MAP Sensor Output Chart

Meets NATEF Task:  (A8-B-7) P-2  Inspect and test sensors, actuators, and circuits using a graphing multimeter (GMM)/digital storage oscilloscope (DSO); perform necessary action.

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

Most vehicle MAP sensors use a 5-volt reference, a signal return and a ground connection.  As the vacuum inside the intake manifold changes, the MAP sensor voltage changes.

- High vacuum (low absolute manifold pressure) = low voltage

- Low vacuum (high absolute manifold pressure) = high voltage

_____  1.  Connect a T-pin to the signal wire connector at the MAP sensor.

_____  2.  Connect the red lead of a digital voltmeter set to read DC volts to the T-pin.  Connect

the black meter lead to a good chassis ground.

_____  3.  Disconnect the vacuum hose from the MAP sensor (or remove the sensor from the

manifold) and attach a hand-operated vacuum pump to the sensor.

_____  4.  Place a dot on the graph that represents the MAP sensor voltage when 5, 10, 15, 20, 25

and 30 in. Hg of vacuum is applied to the sensor.

_____  5.  Connect the dots.  The results should be a straight line.

OK _____    NOT OK _____

0                  5                  10                  15                 20                 25                 30

VACUUM APPLIED (in. Hg)

_____  6.  Based on the results of this test, what is the necessary action? ___________________

_________________________________________________________________