Fuel Pump Current Ramping

Meets NATEF Task:  (A8-D-3) P-1  Inspect and test fuel pumps and pump control systems for pressure, regulation, and volume; perform necessary action.

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

_____  1.  Check service information for the specified fuel pump operating speed (normally from

3500 to 7500 RPM).

______________________________________

_____  2.  Tools and equipment needed to determine

the rotational speed of the fuel pump include:

____  Digital storage oscilloscope

____  Current clamp

____  Fused jumper lead

_____  3.  Perform a current ramping procedure and determine the following:

____  Number of commentator segments = ______ (usually 8, 10, or 12)

____  Milliseconds needed for one rotation of the pump = ______

____  Fuel pump speed = 60,000 ÷ milliseconds = _______

_____  4.  Based on the test performed, what is the necessary action?  ___________________

_______________________________________________________________

_______________________________________________________________