Cylinder Bore Deglazing

Meets ASE Task:  (A1-C-5) P-2  Deglaze and clean cylinder walls.

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

A deglazing hone is designed to remove the hard surface glaze in the cylinder.  A deglazing hone is flexible so that it can follow the shape of the cylinder and cannot be used to straighten the cylinder.

_____  1.  Completely disassemble the engine block.

_____  2.  Measure the cylinder for out-of round.

Maximum out-of-round specification = ___________

Actual out-of-round:

cylinder #1 _________	cylinder #5 __________

cylinder #2 _________	cylinder #6 __________

cylinder #3 _________	cylinder #7 __________

cylinder #4 _________	cylinder #8 __________

OK _____     NOT OK _____

_____  3.  Measure the cylinder for taper.

Specifications = ___________

Actual cylinder taper:

cylinder #1 _________	cylinder #5 __________

cylinder #2 _________	cylinder #6 __________

cylinder #3 _________	cylinder #7 __________

cylinder #4 _________	cylinder #8 __________

OK _____     NOT OK _____

_____  4.  If both cylinder taper and out-of-round measurements are within factory

specifications, select a deglazing hone of the proper size with a 220 or 280 grit stone.

_____  5.  Install the hone into an electric drill motor and hone the cylinders being sure to use the

proper coolant/lubricant specified by the manufacturer of the hone.

_____  6.  After honing, be sure to wash the block with soap or detergent to thoroughly clean all

of the honing grit from the block.