Alternator Rotor Testing

Meets ASE Task:  (Not specified by ASE)

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

_____  1.  Carefully inspect the rotor for damage.

OK _____	NOT OK _____

_____  2.  Use 400 grit emery cloth to clean the slip rings.

Be sure to rotate the slips in the cloth

to avoid creating flat areas.

_____  3.  Set a digital multimeter (DMM) to read ohms (low

scale).

_____  4.  Measure the resistance between the slip rings and compare with specifications:

GM              	   =  2.2 to 3.5 (

actual = __________			Ford              	   =  3.0 to 5.5 (

Chrysler              =  3.0 to 6.0 (

OK _____	NOT OK _____

_____  5.  To test that the rotor winding is not shorted-to-ground, place one meter lead on a slip

ring and the other meter lead to the steel shaft of the rotor.  The reading should be

infinity (OL) if the rotor is OK.

reading = _____________		OK _____	NOT OK _____

Shorted-to-ground                                                            Open