Micrometer

Meets ASE Task:  (Not specified by ASE)

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

A micrometer is the most used measuring instrument in engine service and repair.  The thimble rotates over the barrel on a screw that has 40 threads per inch.  Every revolution of the thimble moves the spindle 0.025 inch.  The thimble is graduated into 25 equally spaced lines; therefore, each line represents 0.001 inch.  Measure and record the following engine components.

_____  1.  Pushrod diameter = _____________

_____  2.  Intake valve stem diameter = ___________

_____  3.  Exhaust valve stem diameter = __________

_____  4.  Camshaft bearing diameter = ________

_____  5.  Piston diameter = _________________

Check the factory specifications for

exact location on the piston to measure

the diameter.

Location = ______________________

_____  6.  Crankshaft main bearing journal diameter = ________________

_____  7.  Crankshaft rod bearing journal diameter = _________________