Disarm and Enable Airbags

Meets ASE Task:  (A6-G-4) P-1  Disarm and enable the airbag system for vehicle service.

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

Airbags should be temporarily disabled whenever working

on or around the steering column or dash areas of a vehicle

equipped with airbags.

_____  1.  Check service information for the specified method

to use to disarm and enable the airbags.

______________________________________

______________________________________

______________________________________

_____  2.  Disconnect the negative (-) battery cable.

_____  3.  Locate and remove the airbag fuse.

Label of fuse = ________________________

Amperage rating of the fuse = ____________

_____  4.  Remove the covering from underneath the steering column to gain access to the

steering column airbag wiring connector.

_____  5.  Disconnect the yellow airbag electrical connector.

_____  6.  Locate and disconnect the yellow passenger side airbag electrical connector.

Describe the location __________________________________________

What components had to be removed to gain access to the passenger side airbag connector?  ___________________________________________

_____  7.  After servicing the steering column or dash, restore the airbags by reconnecting the

connectors, installing the airbag circuit fuse, and reconnecting the battery.

_____  8.  Start the engine and check for proper operation of the airbag warning light.

OK _____     NOT OK _____