Heating System Performance Check

Meets ASE Task:  (A7-C-2) P-2, (A7-C-3) P-2  Diagnose temperature control problems; determine needed action.

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

_____  1.  Check the front of the radiator and air-conditioning condenser for debris that could

limit airflow.  Clean as required.

OK_____		NOT OK_____

_____  2.  Perform a thorough visual inspection of the cooling system.  Look for hoses that may

be leaking, cut, or swollen.

OK_____		NOT OK_____

_____  3.  Start the engine and operate the heater and air-conditioning controls for proper

operation including:

defroster (airflow to windshield)	OK_____		NOT OK_____

heater (airflow to floor) 		OK_____		NOT OK_____

A/C (airflow to vents) 		OK_____		NOT OK_____

blower motor on all speeds		OK_____		NOT OK_____

_____  4.  Using an infrared pyrometer, measure the temperature of the upper radiator hose.

Temperature = ________ (should be close to the same temperature as the

thermostat rating)

OK_____		NOT OK_____

_____  5.  Based on the test results, what is the needed action?  __________________________

_________________________________________________________________