Cooling System Inspection

Meets ASE Task:  (A7-C-1) P-1, (A7-C-2) P-2  Perform cooling system pressure tests; perform needed action.

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

_____  1.  Check the level of coolant in the coolant recovery tank.  It should be between the “full

hot” and “full cold” lines.

OK_____		NOT OK_____

_____  2.  After the engine has cooled, remove the radiator cap.

CAUTION:  Do not remove the radiator cap if the engine is hot.  The coolant will explosively expand when the cap is removed which can cause severe burns to anyone near the vehicle.

_____  3.  The coolant should be at the full level in the radiator.

OK_____		NOT OK_____

_____  4.  Check the freezing point and boiling point of the coolant.

Freezing point = ___________  [should be -34( F (-36( C) or lower]

Boiling point = ___________

OK_____		NOT OK_____

_____  5.  Pressure test the cooling system by installing a

cooling system pressure tester and pump until

the pressure is equal to the pressure cap value.

Pressure should hold if there are no leaks.

OK_____		NOT OK_____

_____  6.  Test the radiator cap using the cooling system

pressure tester with an adapter that fits the cap.

The cap should hold its rated pressure.

OK_____		NOT OK_____

_____  7.  What is the needed action? _______________________________________________