Scan Tool Testing of the Ignition System

Meets ASE Task:  (A8-C-1) P-2 Diagnose electronic ignition-related problems; determine needed action.

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

_____  1.  Check service information for the recommended procedures to follow when using a

scan tool to monitor what the vehicle computer is looking at and what commands are

being sent to the various engine actuators and components.

_____  2.  Connect the scan tool to the data link connector (DLC) of the vehicle and scroll

through the various parameters until engine RPM and ignition spark timing can

be viewed.

Idle RPM = _____                             Spark advance at idle = _____

_____  3.  Slowly increase engine speed and observe the amount of spark advance.

Spark advance at 1000 RPM = _______ degrees

Spark advance at 1500 RPM = _______ degrees

Spark advance at 2000 RPM = _______ degrees

Spark advance at 2500 RPM = _______ degrees

_____  4.  Scroll the display of the scan tool until knock sensor (KS) activity or timing retard is

displayed (if the vehicle is so equipped).

KS signal at idle = _______ (should be zero) (The engine should not have

detected an engine knock.)

_____  5.  Increase engine speed while observing KS or timing retard amount.  Did the computer

retard timing?

Yes _____  No _____

_____  6.  Lightly tap on the engine block and observe KS or timing retard with the engine

warmed above idle speed.  Was a knock detected?

Yes _____  No _____

_____  7.  Based on the test results, what is the needed action? ___________________________