PCV System Diagnosis

Meets ASE Task:  (A8-E-1) P-3  Inspect, test and service positive crankcase ventilation (PCV) filter/breather cap, valve, tubes, orifices, and hoses; perform needed action.

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

_____  1.  Check service information for the

recommended procedures to follow when

diagnosing the PCV system.

_____________________________

_____________________________

_____  2.  Start the engine and allow it to idle and remove the oil fill cap.

_____  3.  Place a piece of paper or a 3" x 5" card over the filler.  (The PCV system is

functioning correctly if the paper is held down tight onto the filler by vacuum in the

crankcase).

_____  4.  Seal off the oil fill opening and measure the crankcase

vacuum at the dipstick tube = ________ (should be about 0.5

in. Hg. or 7 in. or more of water if using a water manometer).

OK _____    NOT OK _____

_____  5.  Based on the test results, what is the needed action?

__________________________________________

__________________________________________

__________________________________________