Master Cylinder Service

Meet NATEF Task:  (A5-B-3) P-1, (A5-B-4) P-1 Check master cylinder for external and internal leaks and proper operation; remove, bench bleed, and reinstall master cylinder.

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

_____  1.  Check visually for signs of external brake fluid

leaks.

_____ OK    _____ NOT OK

Describe location _____________________

_____  2.  Check for internal leakage by observing the

level of brake fluid in the front compared

to the rear.

A.  Is the level higher in the front than the rear?  ____ Yes   ____ No

B.  Is the brake pedal lower than normal?   ____ Yes   ____ No

If yes to both A and B above, then the master cylinder is leaking internally and must

be replaced.

_____  3.  Have an assistant depress the brake pedal while watching the brake fluid in the master

cylinder reservoir.  The brake fluid should be seen to move as the brake pedal is being

depressed if the sealing caps are OK and positioned correctly.

Movement observed?	____ Yes   ____ No

If brake fluid does not move and there is a braking system problem, the master

cylinder or linkage adjustment is faulty.

_____  4.  Based on the test results, what is the needed action? __________________________

_________________________________________________________________