Red Brake Warning Lamp Diagnosis

Meets ASE Task:  (A-5-B-10) P-3, (A5-B-11) P-2  Inspect, test and/or replace components of brake warning light system.

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

_____  1.   Does the vehicle use a brake fluid level sensor?

___ Yes   ___ No

(If yes, describe the location: __________________________________.)

_____  2.   Does the vehicle use a pressure differential

switch?

___ Yes   ___ No

(If yes, describe the location: _________________________________________.)

_____  3.   With the ignition key on, engine off (KOEO), apply the parking brake.  Did the red

brake warning lamp light?

___ Yes   ___ No

(If no, why not? ____________________________________________________)

_____  4.   Unplug the wiring connector from the brake fluid level sensor or pressure differential

switch.  With the key on, engine off (KOEO), did the red brake warning lamp light?

___ Yes   ___ No     (It should not have come on.)

_____  5.  State the vehicle manufacturer’s recommended inspection, testing, and replacement

procedures:

__________________________________________________________________

__________________________________________________________________

__________________________________________________________________

__________________________________________________________________