Vacuum Supply/Manifold or Auxiliary Pump

Meets ASE Task:  (A5-E-2) P-1  Check vacuum supply to vacuum-type power booster.

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

_____  1.  Check service information for the recommended procedures and specifications for

checking vacuum supply to power booster.

_________________________________________________________________

_________________________________________________________________

_________________________________________________________________

_____  2.  Is the vehicle equipped with an auxiliary vacuum pump?     ____ Yes    ____ No

_____  3.  Most vehicle manufacturers specify that a vacuum “T” be installed in the vacuum line

between the intake manifold and/or auxiliary pump and the vacuum power brake

booster assembly.  Most manufacturers specify a minimum of 15 in. Hg. of vacuum be

measured.

Actual vacuum measured at the power brake booster = __________

____  OK    ____ NOT OK