Tire, Wheel, Axle, and Hub Runout

Meets ASE Tasks: (A4-F-4) P-2  Measure wheel, tire, axle flange, and hub runout;

determine needed action.

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

_____  1.  Check service information for the specifications for radial and lateral runout.

Specification for radial runout = _________ (usually less than 0.060 inch).

Specification for lateral runout = _________ (usually less than 0.045 inch).

_____  2.  Using a runout gauge, rotate the tire and record the radial runout (roundness of the

tires) and the lateral runout (side-to-side movement) of the tires.

Tire	      Radial Runout	      Lateral Runout

R.F.      	______ 		_______

R.R.		______  		_______

L.F.		______         		_______

L.R.		______         		_______

_____  3.  Using a dial indicator, measure the axle and hub runout.

Hub runout	= ________		OK ____    NOT OK ____

Flange runout	= ________		OK ____    NOT OK ____

_____  4.  Based on the measurements, what needed action is needed?

______________________________________________________________

______________________________________________________________