Engine Oil Dipstick Test

Meets ASE Task:  (A8-A-4)  P-2  Diagnose oil consumption concerns; determine needed action.

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

_____ 1.  Check the engine oil level and condition.

Level:  ____low     ____okay     ____overfilled

Color:  ____black   ____dark brown     ____amber

_____  2.  Ignite the oil on the dipstick:

_____ does not burn

_____ does burn

NOTE:  If the oil on the dipstick burns, there is gasoline in the oil.  This will

cause the engine to run rich by drawing the fuel through the PCV system.

Gasoline in the oil can also damage the engine due to the diluted oil not properly

lubricating the engine.

_____ 3.  Drip oil onto the hot exhaust manifold:

_____ does not bubble

_____ does bubble

NOTE:  If the oil bubbles on the exhaust manifold, coolant (water) is in the oil.

_____ 4.  Rub the oil from the dipstick between your fingers:

_____ does not feel gritty

_____ does feel gritty

_____  5.  Based on the test results, what is the needed action? _________________________