Accessory Drive Belt Inspection

Meets ASE Task:  (A1-D-3)  P-1  Inspect and adjust drive belts; check pulley alignment.

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

Proper operation of the alternator and the charging system as well as the water (coolant) pump and other cooling systems depend on the accessory drive belt(s).

Serpentine (poly-V) belt:

_____  1.  Check for cracks - replace if more than 3 cracks in any one rib in 3 inches.

_____  2.  Check for proper tension - check the tensioner notch location for proper tension

position.

OK ____   NOT OK ____

V-belts:

_____  1.  Check belt tension:

- usual specifications is 70 to 100 lb. of tension using a belt tension gauge.

- maximum of ½” deflection.

OK ____   NOT OK ____

_____  2.  Check the belt for flaying, cracks and glazing.

OK ____   NOT OK ____

_____  3.  Check pulley adjustment.

OK ____   NOT OK ____