Engine Cooling System Inspection

Meets ASE Task:  (A1-D-1)  P-1  Perform cooling system pressure tests; check coolant condition; inspect and test radiator, pressure cap, coolant recovery tank, and hoses.

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

_____  1.  Inspect the radiator for exterior leaks or clogged areas due to bugs, dirt, or debris, and clean as required.

OK _____	NOT OK _____

_____  2.  Pressure test the cooling system.  The entire

system should hold about 15 psi for 5

minutes, unless there is a leak.

OK _____	NOT OK _____

Location of leak ____________________

_____  3.  Pressure test the radiator cap.  The cap holds _________ psi.

OK _____	NOT OK _____

_____  4.  Check the freezing point of the coolant using an hydrometer    __________

[should be -34( F (-37( C) or lower].

OK _____	NOT OK _____

_____  5.  Check the boiling point of the coolant using an hydrometer = __________.

OK _____	NOT OK _____