Engine Oil Change

Meets ASE Task:  (A1-D-10)  P-1 Perform oil and filter change.

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

_____  1.  Check the owner's manual, service manual, or technical literature to determine the

correct viscosity rating and quantity of oil needed.

- Rcommended viscosity:  SAE _______  or  SAE ________

- Number of quarts (liters):  with the filter ______  without the filter ______

- American Petroleum Institute rating (if specified) ___________

_____  2.  Filter brand and number:    Brand ____________________ Number _____________

_____  3.  Hoist the vehicle safely.  Position the oil drain unit under the drain plug and raise to a

height about 1 foot under the drain plug.

_____  4.  Select the proper size wrench and remove the drain plug and allow the oil to drain into

the drain pan.

_____  5.  After all the oil has been drained, install a new sealing washer (if needed) and install

the drain plug.

_____  6.  Move the oil drain unit under the filter and remove the old oil filter.

_____  7.  Use a shop cloth and clean the oil filter gasket contact area on the engine block.

_____  8.  Apply a thin coating of engine oil to the rubber gasket on the new oil filter.

_____  9. Install the new oil filter and hand tighten about 3/4 turn after the gasket contacts the

engine block.

_____ 10. Lower the vehicle.  Install the recommended quantity of engine oil using a funnel to

prevent spilling oil.  Replace the oil filler cap.

_____ 11. Start the engine and allow it to idle.  The "oil" light should go out within 15 seconds.

_____ 12. Look under the vehicle and check for leaks at the drain plug and the oil filter.

_____ 13. Check the level of the oil again and add as needed.  Caution: Do not overfill!