Exhaust System Smoke Test

Meets ASE Task: (A8-A-4) P-2  Diagnose engine noises and vibrations; determine needed action.

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

_____  1.  Start the smoke machine and allow it to reach operating temperature.

_____  2.  Hoist the vehicle to be able to see the exhaust system.

_____  3.  Insert the discharge hose from the smoke machine into the tailpipe and start the flow

of smoke.

_____  4.  Check for evidence of smoke from parts of the

exhaust system, which indicates a leak.

_____  No smoke visible

_____  Smoke visible (describe the location)

_____________________________

_____  5.  Lower the vehicle and repeat the injection of smoke into the exhaust system.

_____  6.  Check for evidence of smoke from under the hood and around the intake manifold and

exhaust gas recirculation (EGR) valve and piping.

_____  No smoke visible

_____  Smoke visible (describe the location) _____________________________

_____  7.  What is the needed action?  ____________________________________________

_________________________________________________________________

_____  8.  Disconnect the smoke machine.