Cylinder Leakage Test

Meets ASE Task:  (A8-A-8)  P-1  Perform cylinder leakage tests; determine needed action.

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

_____ 1.  The engine should be at normal operating temperature.

_____ 2.  Rotate the engine until the piston of the cylinder being tested is at TDC on the

compression stroke.

_____ 3.  Calibrate the cylinder leakage gauge.

_____ 4.  Install compressed air in the cylinder.  Read the gauge.

_____  % of leakage

Check one:

_____  Good - less than 10%

_____  Acceptable - less than 20%

_____  Unacceptable - higher than 20%

_____ 5.  Check the source of air leakage:

_____  a.  radiator - possible blown head gasket or cracked cylinder head.

_____  b.  tail pipe - defective exhaust valve(s).

_____  c.  carburetor or air inlet - defective intake valve(s).

_____  d.  oil filler cap - possible worn or defective piston rings.

_____  6.  Based on the test results, what is the needed action?  _______________________

________________________________________________________________