Oil Pressure Measurement

Meets ASE Task:  (A1-D-9) P-1   Perform oil pressure test; determine needed action.

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

_____  1.  Locate the oil pressure-sending (sender) unit.

_____  2.  Remove the sending unit using the proper size sending unit socket or wrench.

_____  3.  Thread a mechanical oil pressure gauge into the hole where the sending unit was

located.

_____  4.  Route the oil pressure gauge hose away from the moving components of the engine.

_____  5.  Start the engine and check for leaks.

_____  6.  Record the oil pressure:

oil pressure @ idle _____________

oil pressure @ 1,000 RPM ________

oil pressure @ 2,000 RPM ________

oil pressure @ 3,000 RPM ________

NOTE:  Most engines require about

10 psi per 1,000 RPM.

_____  7.  Results:  (check one)

great_____ (over 10 psi per 1,000 RPM)

good _____ (at 10 psi per 1,000 RPM)

bad  _____ (less than 10 psi per 1,000 RPM)

_____  8.  Based on the test results, what is the needed action?  ________________________

__________________________________________________________________