Cylinder Head Flatness Measurement

Meets ASE Task:  (A1-B-2) P-1 Clean and visually inspect a cylinder head for cracks; check gasket surface areas for warpage and surface finish; check passage condition.

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

_____  1.  What is the maximum allowable out-of-flatness according to factory specifications?

___________________________

_____  2.  Thoroughly clean the fire deck surface of the cylinder head using the appropriate

cleaning method:

- cast iron cylinder heads

bristle discs:

a.  green (coarse – 50 grit)

b.  yellow (medium – 80 grit)

scraper

- aluminum cylinder heads

bristle discs:

a.  yellow (medium – 80 grit)

b.  white (fine – 120 grit)

plastic or wooden scraper

_____  3.  Use a precision straight edge

and a feeler (thickness) gauge

to check for warpage, distortion,

bend and twist by checking in five

places.

_____  4.  Maximum thickness of feeler gauge that could be placed between the straight edge

and the head is _____________inches.

OK _____     NOT OK _____

_____  5.  What is the necessary action? _____________________________________________

_________________________________________________________________