| Application | Year | Bleeding Sequence | ABS? | Drive Wheels | Manual or Pressure | PSI | Remarks |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Domestic Cars |  |  |  |  |  |  |  |
| Daimler Chrysler |  |  |  |  |  |  |  |
| TC by Maserati | 1989-90 | RF, LF, RR, LR |  | Rear | Either | 10-15 | Bleed front normally, bleed rear with key on, system pressurized, and pedal partially depressed.. |
| All Others | 1965-85 | RR, LR, RF, LF |  | Rear | Either | 25-35 | Manual bleeding is preferred, when pressure bleeding vehicle with composite master cylinder use 25 psi max. |
| Premier, Monaco | 1988-92 | RR, LR, RF, LF | No | Front |  | 15-20 | Rear wheels must be on the ground when bleeding. |
| All Others | 1978-94 | RR, LF, LR, RF | No | Front | Either |  |  |
| Avenger, Concord, Intrepid, LHS, |  |  |  |  |  |  |  |
| New Yorker, Sebring, Talon & Vision | 1995-96 | RR, LF, LR, RF | No | Front | Either |  |  |
| Avenger, Sebring & Talon | 1997-99 | RR, LF, LR, RF | No | Front | Either |  |  |
| Breeze, Cirrus, Neon, |  |  |  |  |  |  |  |
| Sebring Convertible & Stratus | 1995-99 | LR, RF, RR, LF | No | Front | Either |  |  |
| Concord, Intrepid, LHS, New Yorker, |  |  |  |  |  |  |  |
| Vision & 300M | 1997-99 | RR, LR, RF, LF | No | Front | Either |  |  |
| w/ABS |  |  |  |  |  |  |  |
| Avenger, Sebring & Talon | 1995-99 | RR, LF, LR, RF | Yes | Front | Either |  |  |
| Bosch | 1988-90 | LR, RR, LF, RF | Yes | Front | Either | 10-15 | Accumulator must be depressurized before bleeding. With key off pump pedal at least 25 times. Stoke pedal slowly with 5 second intervals when manual bleeding. |
| Bendix ABX-4 |  |  |  |  |  |  |  |
| Breeze, Cirrus, Neon, |  |  |  |  |  |  |  |
| Sebring & Stratus | 1995-97 | LR, RF, RR, LF | Yes | Front | Either |  | Bleed base brake system normally. Use DRB to bleed if replacing hydraulic control unit. |
| Bendix-4 | 1993-95 | RR, LF, LR, RF | Yes | Front | Manual |  | Bleed base brake system first. Bleeding modulator requires Diagnostic Readout Box (DRB) or equivalent and special procedure. |
| Bendix-6 | 1991 | RR, LR, RF, LF | Yes | Front | Either | 10-15 | Before bleeding release accumulator pressure. With key off, pump pedal at least 25 times. Bleed load sensing proportioning valve first on vehicles equipped. Bleed master cylinder first if equipped with a bleeder screw. A DRB-II is required to bleed modulator see service manual for procedure. |
| Bendix-6 | 1992-94 | RR, LF, LR, RF | Yes | Front | Either | 10-15 | Before bleeding release accumulator pressure. With key off, pump pedal at least 25 times. Bleed load sensing proportioning valve first on vehicles equipped. Bleed master cylinder first if equipped with a bleeder screw. A DRB-II is required to bleed modulator see service manual for procedure. |
| Bendix-10 | 1990-94 | LR, RR, LF, RF | Yes | Front | Either | 20 | Before bleeding release accumulator pressure. With key off, pump pedal at least 40 times. |
| Teves Mark IV-G | 1995-97 | RR, LF, LR, RF | Yes | Front |  |  | Bleed base brake system normally. Use DRB to bleed if replacing hydraulic control unit. |
| Teves Mark 20 |  |  |  |  |  |  |  |
| Breeze, Cirrus, Neon, |  |  |  |  |  |  |  |
| Sebring Convertible & Stratus | 1998-99 | LR, RF, RR, LF | Yes | Front |  |  | Bleed base brake system normally. Use DRB to bleed if replacing hydraulic control unit. |
| Concord, Intrepid, LHS & 300M | 1998-99 | RR, LR, RF, LF | Yes | Front |  |  | Bleed base brake system normally. Use DRB to bleed if replacing hydraulic control unit. |
| Ford Motor Co. |  |  |  |  |  |  |  |
| RWD w/o ABS | 1965-93 | RR, LR, RF, LF | No | Rear | Either | 10-30 |  |
| Cougar & Thunderbird | 1994-97 | RR, LF, LR, RF | No | Rear | Either | 10-30 |  |
| All Others | 1994-99 | RR, LR, RF, LF | No | Rear | Either | 10-30 |  |
| Crown Victoria, Grand Marquis & |  |  |  |  |  |  |  |
| Town Car | 1990-94 | RR, LF, LR, RF | Yes | Rear |  |  | Use Anti-Lock Breakout Box (T90P-50-ALA) to bleed brakes. Before bleeding brakes, see service manual for charging system procedure. |
| Crown Victoria, Grand Marquis & |  |  |  |  |  |  |  |
| Town Car | 1995-99 | RR, LR, RF, LF | Yes | Rear |  | 10-30 | Bleeding ABS requires the use of New Generation Star (NGS) Tester (007-00500). See service manual for procedures. |
| Cougar & Thunderbird, |  |  |  |  |  |  |  |
| Mark VII & Mark VIII | 1988-92 | RF, LF, RR, LR | Yes | Rear | Manual |  | Front brakes must be bled manually. Allow 5 second intervals between pedal strokes. Accumulator can be charged while bleeding.Acuumulator MUST be fully charged to bleed rears. Key on to allow the accumulator to charge, depress pedal and keep bleeder open for 10 seconds. Fluid pressure will be high. |
| Cougar & Thunderbird, |  |  |  |  |  |  |  |
| Mark VII & Mark VIII | 1988-92 | RF, LF, RR, LR | Yes | Rear | Pressure | 35 | Bleed with key off and pressure released. Bleeder must be open for 10 seconds. |
| Cougar & Thunderbird | 1993-97 | RR, LF, LR, RF | Yes | Rear |  | 10-30 | Anti-Lock Brake Adapter (T90P-50-ALA) is required to bleed ABS. See service manual for procedure. |
| Mark VIII | 1993-96 | RR, LR, RF, LF | Yes | Rear |  | 10-30 | Anti-Lock Brake Adapter (T90P-50-ALA) is required to bleed ABS. See service manual for procedure. |
| Mark VIII | 1997-98 | RR, LR, RF, LF | Yes | Rear |  | 10-30 | New Generation Star (NGS) Tester (007-00500) is required to beed ABS. See service manual for procedure. |
| Mustang | 1994-97 | RR, LR, RF, LF | Yes | Rear | Either | 10-30 |  |
| Mustang | 1998-99 | RR, LR, RF, LF | Yes | Rear |  | 10-30 | New Generation Star (NGS) Tester (007-00500) is required to beed ABS. See service manual for procedure. |
| All Others | 1986-87 | RR, LR, RF, LF | Yes | Rear |  | 35 | Front brakes may be bled manually or with pressure method. Pressure bleeder or accumulator is required to bleed rear brakes. Bleeder screws must be open and predal must be depressed. Then key on, close bleeder screws and key off and stroke pedal. |
| FWD w/o ABS | 1978-94 | RR, LF, LR, RF | No | Front |  | 10-30 | Manual bleeding on model year 1983 and later allow 5 second intervals between pedal strokes. (Not on Probe or Festiva) |
| Contour, Cougar & Mystique | 1995-99 | LF, RR, RF, LR | No | Front | Either | 10-30 |  |
| Continental, Escort, Sable, |  |  |  |  |  |  |  |
| Taurus, Tracer | 1995-99 | RR, LR, RF, LF | No | Front | Either | 10-30 |  |
| Probe | 1995-97 | RR, LF, LR, RF | No | Front | Either | 10-30 |  |
| Continental | 1988-89 | RF, LF, RR, LR | Yes | Front |  | 35 | Front brakes can be bled either manually or with pressure method. Before bleeding, accumulator must be free of pressure. With key off pump pedal hard at least 20 times. Accumulator MUST be fully charged to bleed rears. Key on to allow accumulator to charge, depress pedal and keep bleeder open for 10 seconds. Fluid pressure will be high. |
| Continental, Sable & Taurus | 1990-94 | RR, LF, LR, RF | Yes | Front |  | 10-30 | Pressure must not exceed 50 psi. Between slow pedal strokes allow 5 second intervals when manual bleeding. The Anti-Lock Breakout Box (T90-P-50-ALA) is required to bleed hydraulic control unit and master cylinder. Before bleeding lines accumulator must be free of pressure. With key off pump pedal at least 20 times hard then bleed with pressure method. |
| Continental | 1995-99 | RR, LR, LF, RF | Yes | Front | Either | 10-30 | If Hydraulic Control Unit (HCU) lines have been discconected or HCU is replaced check service manual for bleeding procedures. |
| Contour & Mystique | 1995-97 | RR, LF, LR, RF | Yes | Front | Either | 10-30 | To remove air repeat bleeding sequence. |
| Contour, Cougar & Mystique | 1998-99 | LF, RR, RF, LR | Yes | Front |  | 10-30 | Use New Generation Star (NGS) Tester (007-00500) to bleed system if spongy pedal is still present or replacing hydraulic control unit. |
| Escort & Tracer | 1994-96 | RR, LF, LR, RF | Yes | Front | Either | 10-30 |  |
| Escort & Tracer | 1997-99 | RR, LR, RF, LF | Yes | Front | Either | 10-30 | New Generation Star (NGS) Tester (007-00500) is required to beed ABS. See service manual for procedure. |
| Probe | 1994-96 | RR, LR, RF, LF | Yes | Front | Either | 10-30 |  |
| Sable & Taurus | 1995 | RR, LF, LR, RF | Yes | Front |  | 10-30 | Anti-Lock Brake Adapter (T90P-50-ALA) is required to bleed hydraulic control unit or master cylinder in a 2-step procedure. See service manual for procedure. |
| Sable & Taurus | 1996-99 | RF, LF, LR, RR | Yes | Front |  | 10-30 | New Generation Star (NGS) Tester (007-00500) is required to beed ABS. See service manual for procedure. |
| General Motors |  |  |  |  |  |  |  |
| Buick |  |  |  |  |  |  |  |
| RWD w/o ABS | 1977-85 | RR, LR, RF, LF | No | Rear | Either | 20-25 | Allow 15 second intervals between slow pedal strokes when manually bleeding quick take-up master cylinder equipped 1981 and later models |
| RWD w/o ABS | 1986-92 | RR, LR, RF, LF | No | Rear | Either | 20-25 | Allow 15 second intervals between slow pedal strokes when manually bleeding. When pressure bleeding hold metering valve open. |
| RWD w/o ABS | 1993-96 | RR, LR, RF, LF | No | Rear | Either | 10-30 | Allow 15 second intervals between slow pedal strokes when manually bleeding. When pressure bleeding a Combination Valve Pressure Bleeder Adapter (J-39177) is required. |
| Bosch 2U | 1991-95 | RR, LR, RF, LF | Yes | Rear |  | 20-25 | Proportioning Valve Depressor (J-35856) is required for vehicles equipped with rear drums during pressure bleeding to hold the combination valve stem open. |
| Bosch 5 | 1996 | RR, LR, RF, LF | Yes | Rear | Either | 20-25 | Tech-2 is required to Auto Bleed if spongy pedal is present or replacing hydraulic control unit. See service manual for procedure. |
| Regal | 1989-92 | RF, RR, LR, LF | No | Front | Either | 20-25 | Allow 15 second intervals between slow pedal strokes when manually bleeding. When pressure bleeding slowly stroke the pedal. |
| Regal | 1993 | RR, LR, RF, LF | No | Front | Either | 20-25 | Allow 15 second intervals between slow pedal strokes when manually bleeding. When pressure bleeding slowly stroke the pedal. |
| Regal | 1994-96 | RR, LF, LR, RF | No | Front | Either | 20-25 | Allow 15 second intervals between slow pedal strokes when manually bleeding. When pressure bleeding slowly stroke the pedal. |
| Regal & Century | 1997-99 | RR, LF, LR, RF | No | Front |  | 30-35 | Allow 15 second intervals between slow pedal strokes when manually bleeding. |
| All Others | 1980-94 | RR, LF, LR, RF | No | Front | Either | 20-25 | Allow 15 second intervals between slow pedal strokes when manually bleeding. To pressure bleed brakes on model years 1986-87, hold open the metering valve. |
| All Others | 1995-99 | RR, LR, RF, LF | No | Front | Either | 20-25 | Allow 15 second intervals between slow pedal strokes when manually bleeding. To pressure bleed brakes on model years 1986-87, hold open the metering valve. |
| Skylark | 1997-99 | RR, LR, RF, LF | No | Front |  | 30-35 | Allow 15 second intervals between slow pedal strokes when manually bleeding. |
| w/ABS |  |  |  |  |  |  |  |
| Bosch 2U | 1991-93 | LF, RF, LR, RR | Yes | Front | Either | 20-25 |  |
| Century, Regal & Skylark | 1991-96 | RR, LR, RF, LF | Yes | Front |  | 35 | Tech-2 is required to place displacement pistons in upper position before bleeding. |
| Century, Regal & Skylark | 1997-98 | RR, LF, LR, RF | Yes | Front |  | 30-35 | Tech-2 is required to place displacement pistons in upper position before bleeding. |
| Century & Regal | 1999 | RR, LF, LR, RF | Yes | Front | Either | 5-10 | Auto Bleeding is necessary when replacing brake pressure modulator valve or if there is air in the lines. See service manual for procedure. |
| LeSabre & Park Avenue | 1991-95 | RR, LR, RF, LF | Yes | Front |  | 20-25 | Allow 15 second intervals between slow pedal strokes when manually bleeding. |
| LeSabre & Park Avenue | 1996-99 | RR, LR, RF, LF | Yes | Front | Either | 20-25 | Tech-2 is required to Auto Bleed system if hydraulic control unit is replaced. |
| Regal | 1989-90 | RF, LF, RR, LR | Yes | Front | Manual |  | System must be free of pressure. With key off pump pedal at least 40 times hard. Bleed front brakes then depress pedal slowly. Key on and pedal stroke will pressurize the system. Last bleed the rear breakes and depress pedal slowly to halfway for a duration of 15 seconds. |
| Regal | 1989-90 | RR, LR, RF, LF | Yes | Front | Pressure | 10-35 | Accumulator must be free of pressure before the bleeder is connected. With key off pump pedal at least 40 times hard. Attach pressure bleeder and presssurize to 35 psi. While bleeding make sure to tap the calipers with a rubber mallet. |
| Riviera | 1995-96 | RR, LR, RF, LF | Yes | Front |  | 20-25 | Allow 15 second intervals between slow pedal strokes when manually bleeding. |
| Riviera | 1997-99 | RR, LR, RF, LF | Yes | Front | Either | 20-25 | Auto Bleeding is necessary when replacing brake pressure modulator valve or if there is air in the lines. See service manual for procedure. |
| Roadmaster | 1995-96 | RR, LR, RF, LF | Yes | Rear | Either | 20-25 | Tech-2 is required to Auto Bleed if spongy pedal is present or replacing hydraulic control unit. See service manual for procedure. |
| Teves Mark II ABS | 1988-90 | RF, LF, RR, LR | Yes | Front |  | 20 | Front brakes can be bled either manually or with the pressure method one at a time. Accumulator must be free of pressure before bleeding. With key off pump pedal at least 25 times hard. Rear brakes must be pressure bled with accumulator pressurized. Key on and bleed one side at a time while for a 10 second duration depressing the brake pedal. |
| Cadillac |  |  |  |  |  |  |  |
| RWD w/o ABS | 1965-83 | RR, LR, RF, LF | No | Rear | Either | 30 |  |
| RWD w/o ABS | 1984-85 | RR, LR, RF, LF | No | Rear | Manual | 10-15 |  |
| RWD w/o ABS | 1984-85 | RR, LF, LR, RF | No | Rear | Pressure | 30 |  |
| RWD w/o ABS | 1986-92 | RR, LR, RF, LF | No | Rear | Manual | 10-15 | Allow 15 second intervals between slow pedal strokes. |
| RWD w/o ABS | 1986-92 | RR, LF, RF, LF | No | Rear | Pressure | 20-25 | Metering valve must be held open to bleed front brakes. |
| RWD w/o ABS | 1993-96 | RR, LR, RF, LF | No | Rear | Either | 10-30 | Allow 15 second intervals between slow pedal strokes when manually bleeding. When pressure bleeding, Combination Valve Pressure Bleeder (J-39177) is required. |
| Broughham, Fleetwood | 1990-92 | LF, RF, LR, RR | Yes | Rear | Either | 20-25 |  |
| Broughham, Fleetwood | 1995-96 | RR, LR, RF, LF | Yes | Rear | Either | 20-25 | If spongy pedal is still present or hydraulic control unit is replaced see service manual for procedure. |
| Catera | 1997-99 | RR, LR, RF, LF | Yes | Rear | Manual |  | Check service manual for procedure if air is present in the bore of the master cylinder. |
| All Others | 1986-94 | RR, LR, RF, LF | Yes | Rear | Manual | 10-15 | Allow 15 second intervals between slow pedal strokes. |
| All Others | 1986-92 | RR, LF, LR, RF | Yes | Rear | Pressure | 20-25 | If equipped with rear drums, to bleed rear brakes metering valve must be held open. |
| All Others | 1993-94 | RR, LR, RF, LF | Yes | Rear | Pressure | 20-25 | Combination Valve Pressure Bleeder Adapter (J-39177) is required. |
| Cimarron | 1982-85 | RR, LF, LR, RF | No | Front |  | 30 | Vehicles equipped with composite master cylinder, use 20-25 psi. Allow 15 second intervals between slow pedal strokes when manually bleeding. |
| Eldorado & Seville | 1980-85 | RR, LR, RF, LF | No | Front | Either | 30 |  |
| Eldorado & Seville | 1986-90 | RR, LF, LR, RF | No | Front |  | 30 | Vehicles equipped with composite master cylinder, use 20-25 psi. Allow 15 second intervals between slow pedal strokes when manually bleeding. |
| Eldorado & Seville | 1991-94 | LF, RF, LR, RR | No | Front |  | 30 | Vehicles equipped with composite master cylinder, use 20-25 psi. Allow 15 second intervals between slow pedal strokes when manually bleeding. |
| All Others | 1980-94 | RR, LR, RF, LF | No | Front |  | 30 | Vehicles equipped with composite master cylinder, use 20-25 psi. Allow 15 second intervals between slow pedal strokes when manually bleeding. |
| Allante | 1987-92 | LR, RR, LF, RF | Yes | Front | Manual |  | Accumulator must be free of pressure before bleeding, With key off pump pedal at least 25 times hard. Allow 5 second intervals between pedal strokes. Key must be on when bleeding motor and accumulator. |
| Concours, DeVille, Eldorado, |  |  |  |  |  |  |  |
| Fleetwood & Seville | 1995-99 | LF, RF, LR, RR | Yes | Front | Either | 20-25 | Tech-2 is required to Auto Bleed if hydraulic control unit is replaced. See service manual for procedure. |
| Deville, Eldorado, |  |  |  |  |  |  |  |
| Fleetwood & Seville | 1986-90 | RR, LR, RF, LF | Yes | Front |  | 20 | Rear brakes must be bled before front brakes. Accumulator pressure is required, with key on bleed one brake at a time while barely depressing pedal for a 10 second duration. When bleeding the front brakes either manual or pressure bleeding is acceptable. Accumulator must be free of pressure. With key off pump pedal at least 25 times hard. |
| Chevrolet |  |  |  |  |  |  |  |
| Chevette | 1977-85 | LF, RF, LR, RR | No | Rear | Either | 20-30 |  |
| Chevette | 1986-87 | RR, LR, RF, LF | No | Rear | Either | 20-25 |  |
| Corvette | 1965-83 | LR, RR, LF, RF | No | Rear |  | 20-25 | Bleed inner bleeder first if equipped with 2 per brake. To release air, use a rubber mallet to tap calipers. |
| Corvette | 1984-86 | LR, RR, LF, RF | No | Rear |  | 20-25 | When bleeding rear of vehicle must be lower than front. |
| Corvette | 1987-92 | RF, RR, LR, LF | No | Rear | Either | 20-25 | Allow 15 second interval between slow pedal strokes when manual bleeding. Slow pedal strokes are needed for pressure bleeding. |
| Monza & Vega | 1971-80 | RR, LR, RF, LF | No | Rear | Either | 20-30 |  |
| All Others | 1977-92 | RR, LR, RF, LF | No | Rear |  | 20-25 | Vehicles equipped with quick take-up master cylinder, allow 15 second slow pedal stroke intervals when manual bleeding. When pressure bleeding rear brakes metering valve must be held open and Combination Valve Pressure Bleeder Adapter (J-39177) is required. |
| All Others | 1993-94 | RR, LR, RF, LF | No | Rear |  | 10-30 | Vehicles equipped with quick take-up master cylinder, allow 15 second slow pedal stroke intervals when manual bleeding. When pressure bleeding rear brakes metering valve must be held open and Combination Valve Pressure Bleeder Adapter (J-39177) is required. |
| Camaro | 1993-96 | RR, LR, RF, LF | Yes | Rear |  | 30-35 | Tech-1 or Tech-2 is required to place displacement pistons in upper position before bleeding. See service manual for procedure. |
| Camaro | 1997 | RR, LF, LR, RF | Yes | Rear |  | 30-35 | Tech-1 or Tech-2 is required to place displacement pistons in upper position before bleeding. See service manual for procedure. |
| Camaro | 1998 | RR, LF, LR, RF | Yes | Rear | Either | 20-25 |  |
| Camaro | 1999 | RR, LR, RF, LF | Yes | Rear |  | 20-55 | Allow 15 second intervals between slow pedal strokes when manual bleeding. |
| Caprice & Impalla SS | 1995-96 | RR, LR, RF, LF | Yes | Rear | Either | 20-25 | Tech-2 is required to Auto Bleed when hydraulic control unit is replaced. See service manual for procedure. |
| Corvette | 1987-91 | RF, RR, LR, LF | Yes | Rear | Either | 20-25 | Allow 15 second intervals between slow pedal strokes when manual bleeding. When pressure bleeding slowly stroke pedal. |
| Corvette | 1992-94 | RR, LR, RF, LF | Yes | Rear | Either | 20-25 | Allow 15 second intervals between slow pedal strokes when manual bleeding. When pressure bleeding slowly stroke pedal. |
| Corvette | 1995-99 | RR, LR, RF, LF | Yes | Rear | Either | 20-25 | Tech-2 is required to Auto Bleed when hydraulic control unit is replaced. See service manual for procedure. |
| All Others | 1990-92 | RR, LR, RF, LF | Yes | Rear |  | 20-25 | Proportioning Valve Depressor (J-35856) is required for vehicles equipped with rear drums during pressure bleeding to hold the combination valve stem open. |
| Lumina (Except APV Van) | 1990-99 | RR, LF, LR, RF | No | Front |  | 20-25 | Allow 15 second intervals between slow pedal strokes when manual bleeding. |
| Metro & Prizm | 1998-99 | RR, LR, RF, LF | No | Front |  | 20-25 | Allow 15 second intervals between slow pedal strokes when manual bleeding. |
| All Others | 1980-99 | RR, LF, LR, RF | No | Front |  | 20-25 | Allow 15 second intervals between slow pedal strokes when manual bleeding. |
| Beretta, Cavalier, Corsica, Malibu, |  |  |  |  |  |  |  |
| Metro & Prizm (Up To 1997) | 1992-99 | RR, LR, RF, LF | Yes | Front |  | 30-35 | Tech-1 or Tech-2 is required to place displacement pistons in upper position before bleeding. See service manual for procedure. |
| Lumina & Monte Carlo | 1992-99 | RR, LF, LR, RF | Yes | Front |  | 30-35 | Tech-1 or Tech-2 is required to place displacement pistons in upper position before bleeding. See service manual for procedure. |
| Prizm | 1998-99 | RR, LR, RF, LF | Yes | Front | Either | 20-25 | Tech-2 is required to Auto Bleed when hydraulic control unit is replaced. See service manual for procedure. |
| Oldsmobile |  |  |  |  |  |  |  |
| RWD w/o ABS | 1977-85 | RR, LR, RF, LF | No | Rear | Either | 20-25 | Allow 15 second intervals between slow pedal strokes when manual bleeding models with quick take-up master cylinders. (1981 and later) |
| RWD w/o ABS | 1986-92 | RR, LR, RF, LF | No | Rear | Either | 20-25 | To pressurize bleed, hold metering valve open. Wait 15 seconds between slow pedal strokes when manual bleeding. |
| RWD w/o ABS | 1993-94 | RR, LR, RF, LF | No | Rear | Either | 10-30 | Allow 15 second intervals between slow pedal strokes when manual bleeding. Combination Valve Pressure Bleeder Adapter (J-39177) is required when pressure bleeding. |
| RWD w/ABS VI | 1991-94 | RR, LR, RF, LF | Yes | Rear |  | 20-25 | Use a scan tool to place displacement pistons in upper position before bleeding. |
| Toronado, 98 Regency | 1980-85 | RR, LR, RF, LF | No | Front | Either | 20-25 |  |
| Cutlass Supreme | 1989-92 | RF, RR, LR, LF | No | Front | Either | 20-25 | Allow 15 second intervals between slow pedal strokes when manual bleeding. When pressure bleeding stroke pedal slowly. |
| Cutlass Supreme | 1993 | RR, LR, RF, LF | No | Front | Either | 20-25 | Allow 15 second intervals between slow pedal strokes when manual bleeding. When pressure bleeding stroke pedal slowly. |
| All Others | 1980-93 | RR, LF, LR, RF | No | Front | Either | 20-25 | Allow 15 second intervals between slow pedal strokes when manual bleeding. |
| Achieva, Ciera, Cutlass | 1992-99 | RR, LR, RF, LF | Yes | Front |  | 30-35 | Use a scan tool to place displacement pistons in upper position before bleeding. |
| Alero, Cutlass Supreme & Intrigue (3.8L) | 1992-99 | RR, LF, LR, RF | Yes | Front |  | 30-35 | Use a scan tool to place displacement pistons in upper position before bleeding. |
| Aurora | 1995-96 | RR, LR, RF, LF | Yes | Front | Either | 20-25 | Allow 15 second intervals between slow pedal strokes when manual bleeding. |
| Aurora | 1997-99 | RR, LR, RF, LF | Yes | Front | Either | 20-25 |  |
| Cutlass Supreme | 1989-91 | RF, LF, RR, LR | Yes | Front | Manual |  | Depressurize the system, with key off pump the pedal hard at least 40 times then bleed fronts and depress pedal slowly. Next pressurize system with key on by stroking pedal once and bleed rear brakes. For 15 seconds slowly depress pedal halfway. While bleeding tap lightly on front and rear calipers with a rubber mallet. |
| Eighty Eight, Ninety Eight & |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Toronoado | 1986-90 | RF, LF, RR, LR | Yes | Front |  | 20 | Bleed front brakes one at a time. Accumulator must be free of pressure before bleeding. With key off pump pedal at least 25 times hard. Rear brakes must be pressure bled with accumulator pressurized. With key on bleed one at a time and depress pedal for a duration of 10 seconds. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Eighty Eight & Ninety Eight | 1991-95 | RR, LR, RF, LF | Yes | Front |  | 20-25 | Allow 15 second intervals between slow pedal strokes when manual bleeding. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Eighty Eight & Ninety Eight | 1996-99 | RR, LR, RF, LF | Yes | Front | Either | 20-25 | Tech-2 is required to Auto Bleed when hydraulic control unit is replaced. See service manual for procedure. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Intrigue (3.5L) | 1998-99 | RR, LF, LR, RF | Yes | Front | Either | 30-35 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Pontiac |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Fiero | 1984-88 | RR, LR, RF, LF | No | Rear |  | 20-25 | Allow 15 second intervals between slow pedal strokes when manual bleeding. Metering valve must be held open to pressure bleed. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| T1000 | 1981-82 | RR, LF, LR, RF | No | Rear | Either | 20-25 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| T1000 | 1983-87 | RR, LR, RF, LF | No | Rear | Either | 20-25 | Allow 15 second intervals between slow pedal strokes when manual bleeding. Metering valve must be held open to pressure bleed. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| All Others | 1977-92 | RR, LR, RF, LF | No | Rear |  | 20-25 | Allow 15 second intervals between slow pedal strokes when manual bleeding models with quick take-up master cylinders. (1981 and later) Metering valve must be held open when bleeding. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| All Others | 1993-94 | RR, LR, RF, LF | No | Rear |  | 10-30 | Allow 15 second intervals between slow pedal strokes when manual bleeding. Combination Valve Pressure Bleeder Adapter (J-39177) is required when pressure bleeding. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Firebird | 1993-96 | RR, LR, RF, LF | Yes | Rear |  | 30-35 | Tech-1 or Tech-2 is required to place displacement pistons in upper position before bleeding. See service manual for procedure. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Firebird | 1997 | RR, LF, LR, RF | Yes | Rear |  | 30-35 | Tech-1 or Tech-2 is required to place displacement pistons in upper position before bleeding. See service manual for procedure. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Firebird | 1998 | RR, LF, LR, RF | Yes | Rear | Either | 20-25 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Firebird | 1999 | RR, LR, RF, LF | Yes | Rear |  | 20-55 | Allow 15 second intervals between slow pedal strokes when manual bleeding. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Grand Prix | 1989-92 | RF, RR, LR, LF | No | Front |  | 20-25 | Allow 15 second intervals between slow pedal strokes when manual bleeding. When pressure bleeding stroke pedal slowly. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Grand Prix | 1993-94 | RR, LR, RF, LF | No | Front |  | 20-25 | Allow 15 second intervals between slow pedal strokes when manual bleeding. When pressure bleeding stroke pedal slowly. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| All Others | 1980-92 | RR, LF, LR, RF | No | Front |  | 20-25 | Allow 15 second intervals between slow pedal strokes when manual bleeding. Metering valve must be held open to pressure bleed. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| All Others | 1993-94 | RR, LR, RF, LF | No | Front |  | 10-30 | Allow 15 second intervals between slow pedal strokes when manual bleeding. Combination Valve Pressure Bleeder Adapter (J-39177) is required when pressure bleeding. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Grand Am, Sunbird & Sunfire | 1991-99 | RR, LR, RF, LF | Yes | Front |  | 30-35 | Tech-1 or Tech-2 is required to place displacement pistons in upper position before bleeding. See service manual for procedure. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Bonneville & 6000 | 1986-90 | RF, LF, RR, LR | Yes | Front |  | 20 | Bleed front brakes one at a time. Accumulator must be free of pressure before bleeding. With key off pump pedal at least 25 times hard. Rear brakes must be pressure bled with accumulator pressurized. With key on bleed one at a time and depress pedal for a duration of 10 seconds. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Bonneville | 1991-95 | RR, LR, RF, LF | Yes | Front |  | 20-25 | Allow 15 second intervals between slow pedal strokes when manual bleeding. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Bonneville | 1996-99 | RR, LR, RF, LF | Yes | Front | Either | 20-25 | Tech-2 is required to Auto Bleed when hydraulic control unit is replaced. See service manual for procedure. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Grand Prix | 1989-91 | RF, LF, RR, LR | Yes | Front | Manual |  | Depressurize the system, with key off pump the pedal hard at least 40 times then bleed fronts and depress pedal slowly. Next pressurize system by keying on and bleed rear brakes. For 15 seconds slowly depress pedal halfway. While bleeding tap lightly on front and rear calipers with a rubber mallet. |
| Grand Prix | 1992-97 | RR, LF, LR, RF | Yes | Front |  | 30-35 | Tech-1 or Tech-2 is required to place displacement pistons in upper position before bleeding. See service manual for procedure. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Grand Prix | 1998-99 | RR, LF, LR, RF | Yes | Front | Either | 30-35 | Allow 15 second intervals between slow pedal strokes when manual bleeding. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Saturn |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| w/o ABS | 1992-96 | RR, LF, LR, RF | No | Front | Either | 20-25 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| w/Delco VI ABS | 1991-99 | RR, LR, RF, LF | Yes | Front |  | 30-35 | Tech-1 or Tech-2 is required to place displacement pistons in upper position before bleeding. See service manual for procedure. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Domestic Light Trucks |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Daimler Chrysler |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| RWD w/ABS | 1965-86 | RR, LR, RF, LF | Yes | Rear |  | 35 | Vehicles equipped with composite master cylinder, use 25 psi. On model years 1989-94 anti-lock valve(s) must be bled before wheel cylinders. Metering valve stem must be held open to bleed front brakes on all other models. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| RWD w/o ABS | 1965-86 | RR, LR, RF, LF | No | Rear |  | 35 | Vehicles equipped with composite master cylinder, use 25 psi. On model years 1989-94 anti-lock valve(s) must be bled before wheel cylinders. Metering valve stem must be held open to bleed front brakes on all other models. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| RWD w/ABS | 1987-94 | RR, LR, RF, LF | Yes | Rear |  | 20-30 | Vehicles equipped with composite master cylinder, use 25 psi. On model years 1989-94 anti-lock valve(s) must be bled before wheel cylinders. Metering valve stem must be held open to bleed front brakes on all other models. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| RWD w/o ABS | 1987-94 | RR, LR, RF, LF | No | Rear |  | 20-30 | Vehicles equipped with composite master cylinder, use 25 psi. On model years 1989-94 anti-lock valve(s) must be bled before wheel cylinders. Metering valve stem must be held open to bleed front brakes on all other models. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| RWD w/o ABS | 1995-99 | RR, LR, RF, LF | No | Rear | Either | 15-20 | Metering valve stem must be held open to bleed front brakes. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Kelsey-Hayes RWAL | 1995-97 | LR, RR, RF, LF | Yes | Rear | Either | 15-20 | Brakes are bled after combination valve, rear anti-lock valve, and master cylinder. Metering valve stem must be held open to bleed brakes. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Kelsey-Hayes RWAL | 1998-99 | LR, RR, RF, LF | Yes | Rear | Either | 15-20 | Brakes are bled after combination valve, rear anti-lock valve, and master cylinder. Metering valve stem must be held open to bleed brakes. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Kelsey-Hayes EBC-5H-4WAL | 1993-97 | LR, RR, RF, LF | Yes | Rear | Either | 15-20 | Brakes are bled after combination valve, rear anti-lock valve, and master cylinder. Metering valve stem must be held open to bleed brakes. See service manual for procedure to bleed ABS hydraulic control unit. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Kelsey-Hayes EBC-310-4WAL Dakota | 1997 | LR, RR, RF, LF | Yes | Rear |  |  | Base brakes must be manually bled. See service manual for procedure to bleed anti-lock valve assembly. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Kelsey-Hayes EBC-325-4WAL | 1998-99 | RR, LR, RF, LF | Yes | Rear | Either | 15-20 | Brakes are bled after combination valve, rear anti-lock valve, and master cylinder. Metering valve stem must be held open to bleed brakes. See service manual for procedure to bleed ABS hydraulic control unit. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| FWD & AWD Vans w/ABS | 1986-92 | RR, LR, RF, LF | Yes | Front or All |  | 20-30 | Wheel cylinders must be bled after anti-lock valve(s) on model years 1989-92. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| FWD & AWD Vans w/o ABS | 1986-92 | RR, LR, RF, LF | No | Front or All |  | 20-30 | Metering valve must be held open to bleed front brakes. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| FWD & AWD Vans w/o ABS | 1993-99 | RR, LR, RF, LF | No | Front or All | Either | 35 | Correctly adjust rear brakes before manual bleeding. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| FWD & AWD Vans w/ABS Bendix-4 | 1993-94 | RR, LF, LR, RF | Yes | Front or All | Either | 20-30 | If anti-lock valve is present it must be bled before wheels. Pump pedal 40 times hard to release system pressure. ABS must be bled independant of base braking system. Base braking system is bled by normal manual or pressure bleeding. A DRB-II is required to bleed ABS. See service manual for procedure. Base brake system must be bled again after ABS. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| FWD & AWD Vans w/ABS |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Teves Mark IV-G & Teves Mark 20 | 1995-99 | LR, RF, RR, LF | Yes | Front or All | Either |  | If anti-lock valve is present it must be bled before wheels. Pump pedal 40 times hard to release system pressure. ABS must be bled independant of base braking system. Base braking system is bled by normal manual or pressure bleeding. A DRB-II is required to bleed ABS. See service manual for procedure. Base brake system must be bled again after ABS. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Ford Motor Co. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| w/o ABS | 1965-99 | RR, LR, RF, LF | No | Rear | Either | 10-30 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| w/Rear ABS | 1987-99 | RR, LR, RF, LF | Yes | Rear |  | 10-30 | Rear brakes must be bled first, followed by rear anti-lock valve, then front brakes. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| w/4-Wheel ABS |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Bronco, Explorer & Ranger | 1993-96 | RR, LR, RF, LF | Yes | Rear | Either | 10-30 | If run dry, bleed master cylinder first. If hydraulic control unit (HCU) brake lines have been disconnected or if HCU has been replaced then ABS requires special bleeding. See service manual for procedure. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| w/4-Wheel ABS |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Econoline, Expedition, F Series Pickup |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Navigator & 1997-99 Explorer, |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Ranger & Mountaineer | 1994-99 | RR, LR, RF, LF | Yes | Rear | Either | 10-30 | If run dry, bleed master cylinder first. If hydraulic control unit (HCU) brake lines have been disconnected or if HCU has been replaced then ABS requires special bleeding. See service manual for procedure. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| w/o ABS | 1993 | RR, LR, RF, LF | No | Front | Either | 10-30 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Villager | 1994-95 | LF, RF, LR, RR | No | Front | Either | 10-30 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Windstar | 1995-99 | RR, LF, LR, RF | No | Front | Either | 10-30 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Villager | 1995-99 | LF, RF, LR, RR | Yes | Front | Either | 10-30 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Windstar | 1995-96 | LF, RF, LR, RR | Yes | Front | Either | 10-30 | New Generation Star (NGS) Tester is required when bleeding ABS system. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| General Motors |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| RWD w/o ABS | 1965-85 | RR, LR, RF, LF | No | Rear | Either | 20-30 | On model year 1990-92 C/K models equipped with power brakes, isolation/dump valve must be bled after bleeding wheels. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| RWD w/o ABS | 1986-96 | RR, LR, RF, LF | No | Rear | Either | 20-25 | Allow 15 second intervals between slow pedal strokes when manually bleeding. Metering valve stem on the combination valve must be depressed to bleed front brakes when pressure bleeding. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| RWD w/ Rear Wheel ABS | 1987-95 | RR, LR, RF, LF | Yes | Rear |  | 20-25 | Allow 15 second intervals between slow pedal strokes when manually bleeding. Isolation/dump valve must be bled after bleeding wheels. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| RWD w/4-Wheel ABS (Except Tracker) | 1990-99 | RR, LR, RF, LF | Yes | Rear | Either | 20-25 | Master cylinder must be bled first if replaced. Allow 10-15 second intervals between pedal strokes when manual bleeding. Combination valve stem must be held open when pressure bleeding. It is not recommended to vacuum or gravity bleed. See service manual for special procedure if replacing Brake Pressure Modulator Valve or Electro-Hydraulic Unit. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| RWD w/4-Wheel ABS (Tracker) | 1998 | RR, LR, RF, LF | Yes | Rear |  | 20-25 | Tech-2 is required to place displacement pistons in upper position. See service manual for procedure. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| RWD w/4-Wheel ABS (Tracker) | 1999 | RR, LR, RF, LF | Yes | Rear | Either | 20-25 | See service manual for auto bleed procedure if air is in lines or replacing brake pressure modulator valve. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| FWD w/o ABS | 1990-92 | RR, LR, RF, LF | No | Front | Either | 20-25 | Allow 15 second intervals between slow pedal strokes when manually bleeding. When pressure bleeding, metering valve stem must be held open. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| FWD w/o ABS | 1993-94 | RR, LF, LR, RF | No | Front |  | 20-25 | Allow 15 second intervals between slow pedal strokes when manually bleeding. Metering valve stem on the combination valve must be depressed to bleed front brakes when pressure bleeding. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| FWD w/Delco VI ABS | 1992-96 | RR, LR, RF, LF | Yes | Front |  | 30-35 | Tech-2 is required to place displacement pistons in upper position. See service manual for procedure. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| FWD w/Delco VI ABS | 1997-99 | RR, LF, LR, RF | Yes | Front |  | 30-35 | Tech-2 is required to place displacement pistons in upper position. See service manual for procedure. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| International Harvester |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| All Models | 1965-86 | RR, LR, RF, LF | No | Front or Rear | Either | 15-25 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Jeep |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| w/o ABS | 1978-99 | RR, LR, RF, LF | No | 4WD |  | 10-15 | If equipped with metering valve, must be held open when bleeding. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| w/ABS | 1990-94 | RR, LR, RF, LF | Yes | 4WD | Manual | 10-15 | Hydraulic control unit and master cylinder must be bled before brakes. Allow 5 second intervals between slow pedal strokes. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Cherokee, Grand Cherokee & Wrangler | 1995-96 | RR, LR, RF, LF | Yes | 4WD |  |  | Base brakes must be manually bled. DRB must be connected to data link connector (DLC). Select Teves ABS brakes/bleed brakes, then disconnect DRB and bleed base brakes again. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Wrangler | 1997-99 | RR, LR, RF, LF | Yes | 4WD |  |  | Base brakes must be manually bled. DRB-III must be connected to data link connector (DLC). Select Teves ABS brakes/bleed brakes, then disconnect DRB-III and bleed base brakes again. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Cherokee & Grand Cherokee | 1997-99 | RR, LR, RF, LF | Yes | 4WD | Either | 10-15 | Base brakes may be bled manually or by the pressure method. DRB-III must be connected to data link connector (DLC). Select antilock brakes, miscelaneous, then ABS brakes. Follow directions until it says test complete, then disconnect DRB-III and bleed base brakes again. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Import Car & Light Truck |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Acura |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| w/o ABS | 1986-89 | LF, RR, RF, LR | No | Front | Manual | 10-15 | Fluid level must be checked frequently. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| w/o ABS | 1990-96 | RR, LF, LR, RF | No | Front | Manual | 10-15 | Fluid level must be checked frequently. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Integra, Legend & Vigor | 1988-96 | RR, LF, LR, RF | Yes | Front | Manual |  | If modulator requires bleeding see service manual for procedure. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Integra | 1997-99 | LF, RF, RR, LR | Yes | Front | Manual |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 2.2CL & 3.0CL | 1997 | RR, LF, LR, RF | Yes | Front | Manual |  | If modulator requires bleeding see service manual for procedure. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 2.2CL & 3.0CL | 1998-99 | LF, RF, RR, LR | Yes | Front | Either |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 3.5RL | 1996-99 | LF, RF, RR, LR | Yes | Front | Manual |  | If modulator requires bleeding see service manual for procedure. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 2.5TL & 3.2TL | 1995-98 | LF, RF, RR, LR | Yes | Front | Manual |  | If modulator requires bleeding see service manual for procedure. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 3.2TL | 1999 | LF, RF, RR, LR | Yes | Front | Either |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| SLX (4-Wheel ABS) | 1996-99 | RR, LR, RF, LF | Yes | Front |  |  | See service manual for special procedure. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Alfa Romeo |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| All Models | 1965-94 | RF, RR, LR, LF | No |  | Manual | 10-15 | First bleed right side at the same time, then left side at the same time. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Audi |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 4000, 5000, Quattro | 1978-85 | RR, LR, RF, LF | No | AWD | Manual | 10-15 | Hight-sensing brake pressure regualtor lever must be pushed towards rear axle before bleeding. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| All Others | 1986-92 | RR, LR, RF, LF | No | AWD | Manual | 10-15 | DOT-4 brake fluid is required. Brake pressure regulator level must be pushed towards real axle before bleeding. Engine must be running and with hard pedal strokes after sequence rebleed RR on 5000 V8 Quattro models. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| w/ABS & w/o Traction Control | 1986-89 | RR, LR, RF, LF | Yes | AWD | Manual | 10-15 | System must be free of pressure before bleeding. With key off brake pedal must be pumped 20-25 times. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| w/ABS & w/o Traction Control | 1990-96 | RR, RF, LR, LF | Yes | AWD | Manual | 10-15 | System must be free of pressure before bleeding. With key off brake pedal must be pumped 20-25 times. Brake pressure regulator must be pushed towards rear axle before bleeding. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| w/ABS & Traction Control | 1996-99 | RR, LR, RF, LF | Yes | AWD | Pressure |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Austin Healey |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 3000 | 1965-87 | RR, LR, RF, LF | No |  | Manual | 10-15 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| BMW |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| w/o ABS | 1965-85 | RR, LR, RF, LF | No | Rear | Manual | 10-15 | If vehicle is equipped with remote servo, cylinders attached to it must be bled first. If calipers are equipped with 2 bleeders, inner is bled first, followed by outer. If calipers are equipped with 3 bleeders, lower inboard is bled first, followed by other 2 together. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| w/o ABS | 1986-92 | RR, LR, RF, LF | No | Rear | Pressure | 28 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 7 Series W/ASC + T | 1990-94 | RR, LR, LF, RF | Yes | Rear | Pressure | 28 | Sharply pump pedal 20 times with a 2-3 second hold duration between pumps. Now rears must be bled. Pedal must be held down hard, then open bleeder. Repeat this process 10 times. This procedure must be repeated for each wheel in sequence. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| All Others | 1986-99 | RR, LR, RF, LF | Yes | Rear | Pressure | 28 | Open RR bleeder with pedal held down. Slowly pump pedal completely with bleeder open 12 times, hold on floor and close bleeder. Process must be repeated on remaining wheels in sequence. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Chrysler/Eagle Imports |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Conquest | 1986-89 | RR, LR, RF, LF |  | Rear |  | 10-15 | Before bleeding front brakes, bleed modulator on vehicles that are equipped. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| All Others | 1971-85 | RR, LR, RF, LF |  | Rear |  | 10-15 | Bleeding of RR is not required on model Arrow equipped with drum brakes. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Champ | 1979-85 | LR, RF, RR, LF |  | Rear |  | 10-15 | Fluid level must be checked frequently. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Colt Hatchback, Vista, Eagle Vista, |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Wagon w/ABS | 1979-94 | LR, RF, RR, LF | Yes | Front | Manual |  | Engine must be running. If necessary, bleed master clyinder first. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Colt Hatchback, Vista, Eagle Vista, |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Wagon w/o ABS | 1979-94 | LR, RF, RR, LF | No | Front | Manual |  | Engine must be running. If necessary, bleed master clyinder first. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Colt/Summit 200 Series | 1989-93 | LR, RF, RR, LF |  | Front | Manual |  | Engine must be running. If necessary, bleed master clyinder first. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Colt/Summit 200 Series | 1994 | RR, LF, LR, RF |  | Front | Manual |  | Engine must be running. If necessary, bleed master clyinder first. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Summit | 1995-96 | RR, LF, LR, RF |  | Front | Manual |  | Engine must be running. If necessary, bleed master clyinder first. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Summit Wagon | 1995-96 | LR, RF, RR, LF |  | Front | Manual |  | Engine must be running. If necessary, bleed master clyinder first. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Lazer & Talon | 1990-98 | RR, LF, LR, RF |  | Front | Manual |  | Engine must be running. If necessary, bleed master clyinder first. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Stealth | 1991-96 | RR, LF, LR, RF |  | Front | Manual |  | Engine must be running. If necessary, bleed master clyinder first. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 2WD Light Truck | 1978-86 | RR, LR, RF, LF |  | Rear |  | 10-15 | Fluid level must be checked frequently. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Ram Raider | 1987-89 | RR, RF, LF |  | Rear |  | 10-15 | Both rear wheels are controlled by RR bleeder. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| All Other Light Trucks | 1982-96 | RR, LSPV, RF, LF |  | Rear | Manual | 10-15 | LR is controlled by bleeding Load Sensing Proportioning Valve (LSPV). |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Diahatsu |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| All Models | 1988-92 | RR, LR, RF, LF | Yes |  | Manual | 10-15 | If equipped with ABS, rear brakes must be bled with engine running. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Fiat |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| All Models | 1965-82 | RR, LR, RF, LF |  |  | Manual | 10-15 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Ford Motor Co. Imports |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Aspire | 1994-97 | RR, LF, LR, RF |  | Front |  | 10-30 | If master cylinder needs bled, bleed first. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Capri | 1991-94 | RR, LF, LR, RF |  |  | Either | 10-30 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Courier | 1972-82 | RR, LR, RF, LF |  |  | Manual | 10-15 | Lower wheel cylinders must be bled before uppers. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Festiva | 1988-93 | RR, LF, LR, RF |  | Front | Either | 10-30 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Merkur XR4Ti | 1985-89 | RR, LR, RF, LF |  |  |  | 10-15 | Allow 5 second intervals between pedal strokes. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Scorpio | 1988-89 | LF, RF, LR, RR |  |  |  |  | Front brakes must be manually bled. Key off and remove system pressure by pumping brake pedal several times before rear brakes can be bled. In order to bleed rear brakes, open LR bleeder and hold pedal half way down. Key on to operate pump and close bleeder when no air bubbles are present. Repeat procedure on RR. System is under high pressure. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| General Motors Import |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| LeMans | 1988-93 | RR, LF, LR, RF |  | Front |  | 20-25 | Allow 15 second intervals between pedal strokes when manual bleeding. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Metro/Sprint w/o ABS | 1985-97 | RR, LF, LR, RF | No | Front | Manual | 10-15 | Fluid level must be checked frequently. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Metro/Sprint w/Delco VI ABS | 1995-97 | RR, LR, RF, LF | Yes | Front |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Nova | 1985-88 | RR, LF, LR, RF |  | Front |  | 10-15 | Tech-2 is required to place displacement pistons in upper position. See service manual for procedure. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Prizm/Storm w/o ABS | 1989-97 | RR, LR, RF, LF | No | Front |  | 20-25 | Fluid level must be checked frequently. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Prizm/Storm w/Delco VI ABS | 1995-97 | RR, LR, RF, LF | Yes | Front |  | 20-25 | Allow 15 second intervals between pedal strokes when manual bleeding. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Spectrum | 1985-89 | LF, RR, RF, LR |  | Front | Manual | 20-25 | Engine must be running when manual bleeding. If not could damage booster servo. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Tracker w/o ABS | 1989-93 | RF, LF, LR, LSPV | No | Rear | Manual |  | Master cylinder and pressure limiting valve must be bled first if necessary. RR is bled through LSPV. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Tracker w/Rear ABS | 1989-93 | RF, LF, LR, LSPV | Yes | Rear | Manual |  | Master cylinder and pressure limiting valve must be bled first if necessary. RR is bled through LSPV. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Tracker w/o ABS | 1994-97 | RR, LR, RF, LF | No | Rear |  | 20-25 | Master cylinder, proportioning/differential valve, and pressure limiting valve must be bled first if necessary. Allow 15 second intervals between slow pedal strokes when manual bleeding. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Tracker w/Rear ABS | 1994-97 | RR, LR, RF, LF | Yes | Rear |  | 20-25 | Master cylinder, proportioning/differential valve, and pressure limiting valve must be bled first if necessary. Allow 15 second intervals between slow pedal strokes when manual bleeding. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Tracker w/4-Wheel ABS | 1996-97 | RR, LR, RF, LF | Yes | Rear |  | 20-25 | Tech-2 is required to place displacement pistons in upper position. See service manual for procedure. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Honda |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Accord | 1990-93 | LR, RF, RR, LF | Yes | Front |  | 10-15 | Use Bleeder T-wrench and special ABS tester to bleed modulator first if necessary. See service manual for procedure. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Accord | 1990-93 | LR, RF, RR, LF | No | Front |  | 10-15 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Accord | 1994-97 | RR, LF, LR, RF | Yes | Front | Either |  | See service manual for procedure to beed modulator in necessary. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Accord | 1994-97 | RR, LF, LR, RF | No | Front | Either |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Accord | 1998-99 | LF, RF, RR, LR |  | Front | Manual |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Civic | 1990-95 | RR, LF, LR, RF | Yes | Front |  | 10-15 | See service manual for procedure to beed modulator in necessary. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Civic | 1990-95 | RR, LF, LR, RF | No | Front |  | 10-15 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Civic | 1996-99 | RR, LF, LR, RF |  | Front | Manual |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Civic Del Sol | 1993-97 | RR, LF, LR, RF | Yes | Front | Either |  | Special ABS tester required to bleed modulator if necessary. See service manual for procedure. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Civic Del Sol | 1993-97 | RR, LF, LR, RF | No | Front | Either |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| CR-V | 1997-99 | LF, RF, RR, LR |  |  | Manual |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Odyssey | 1995-97 | RR, LF, LR, RF | Yes | Front | Either |  | See service manual for procedure to beed modulator in necessary. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Odyssey | 1995-97 | RR, LF, LR, RF | No | Front | Either |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Odyssey | 1998-99 | LF, RF, RR, LR |  | Front | Manual |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Passport w/Rear ABS | 1994-96 | ALV, LR, RR, LF, RF | Yes | Rear |  |  | Engine must be running while bleeding system, rear Anti-Lock Valve (ALV) must be bled first. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Passport w/4-Wheel ABS | 1996-97 | RR, LR, RF, LF | Yes | Rear |  |  | Tech-2 is required to place displacement pistons in upper position. See service manual for procedure. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Passport w/4-Wheel ABS | 1998-99 | RR, LR, RF, LF | Yes | Rear |  |  | See service manual for special procedure. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Prelude | 1990 | LF, RR, RF, LR | Yes | Front | Either | 10-15 | See service manual for procedure to beed modulator in necessary. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Prelude | 1990 | LF, RR, RF, LR | No | Front | Either | 10-15 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Prelude | 1991-96 | RR, LF, LR, RF | Yes | Front | Either | 10-15 | See service manual for procedure to beed modulator in necessary. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Prelude | 1991-96 | RR, LF, LR, RF | No | Front | Either | 10-15 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Prelude | 1997-99 | LF, RF, RR, LR |  | Front | Manual |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| All Other Models | 1975-89 | LF, RR, RF, LR |  |  | Manual | 10-15 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Hyundai |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| All Models | 1987-98 | LR, RF, RR, LF | No | Front | Either | 10-15 | Brake pedal must not be depressed when pressure bleeding. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Accent | 1999 | LR, RF, RR, LF | No | Front | Manual |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Elantra, Sonata, & Tiburon | 1999 | RR, LF, LR, RF | No | Front | Manual |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Sonata | 1992-94 | RR, LF, LR, RF | Yes | Front |  | 22-23 | Special tester is required to bleed accumulator. See service manual for procedure. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| All Other Models | 1995-98 | LR, RF, RR, LF | Yes | Front | Manual |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Accent | 1999 | LR, RF, RR, LF | Yes | Front | Manual |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Elantra, Sonata, & Tiburon | 1999 | RR, LF, LR, RF | Yes | Front |  |  | Factory scan tool is required to bleed hydraulic control unit. See service manual for procedure. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Infiniti |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| G20 | 1991-99 | RR, LF, LR, RF | Yes | Front | Manual |  | ABS acctuator connectors must be disconnected or battery must be disconnected. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| G20 | 1991-99 | RR, LF, LR, RF | No | Front |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| I30 | 1996-99 | RR, LF, LR, RF | Yes | Front | Manual |  | ABS acctuator connectors must be disconnected or battery must be disconnected. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| I30 | 1996-99 | RR, LF, LR, RF | No | Front |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| J30 | 1993-97 | RR, LR, RF, LF |  | Front | Either | 10-15 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| M30 & Q45 w/o Traction Control | 1990-96 | RR, LR, RF, LF | Yes | Front | Either | 10-15 | Bleed wheels first, then bleed front ABS accuator port, then rear ABS accuator port. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| M30 & Q45 w/Traction Control | 1995-96 | RR, LR, RF, LF |  | Front |  |  | If traction control accuator is replaced, bleed first. See service manual for procedure. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| M30 & Q45 w/ABS & Traction Control | 1997-99 | RR, LR, RF, LF | Yes | Front | Manual |  | ABS acctuator connectors must be disconnected or battery must be disconnected. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| M30 & Q45 w/o ABS & Traction Control | 1997-99 | RR, LR, RF, LF | No | Front |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| QX4 | 1997-99 | LSV, LR, RR, LF, RF | Yes | Front | Manual |  | ABS acctuator connectors must be disconnected or battery must be disconnected. Load Sensing Valve (LSV) must be bled before wheel brakes. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| QX4 | 1997-99 | LSV, LR, RR, LF, RF | No | Front |  |  | Load Sensing Valve (LSV) must be bled before wheel brakes. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Isuzu & LUV |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Amigo, Pickup & Rodeo | 1988-89 | LR, RR, LF, RF |  | Rear | Manual |  | Engine must be running while bleeding. If equipped with Load Sensing Proportioning Valve (LSPV), bleed before front brakes. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Amigo, Pickup & Rodeo w/Rear ABS | 1990-95 | ALV, LR, RR, LF, RF | Yes | Rear | Manual |  | Engine must be running while bleeding. If equipped with rear Anit-Lock Valve (ALV), bleed first. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Amigo, Pickup & Rodeo | 1990-95 | ALV, LR, RR, LF, RF | No | Rear | Manual |  | Engine must be running while bleeding. If equipped with rear Anit-Lock Valve (ALV), bleed first. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Amigo, Pickup & Rodeo w/4-Wheel ABS | 1996-97 | RR, LR, RF, LF | Yes | Rear |  |  | Tech-2 is required to place displacement pistons in upper position. See service manual for procedure. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Amigo, Rodeo, & VehiCROSS | 1998-99 | RR, LR, RF, LF |  | Rear |  |  | See service manual for special procedure. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Hombre w/4-Wheel ABS | 1996-99 | RR, LR, RF, LF | Yes | Rear | Either | 20-25 | Master cylinder must be bled first if replaced. Allow 15 second intervals between slow pedal strokes when manual bleeding. Combination valve stem must be held open when paressure bleeding. It is not recommended to gravity or vacuum bleed. If replacing Brake Pressure Modulator Valve, see service manual for procedure. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Impulse | 1983-89 | LR, RR, RF, LF |  |  | Manual |  | Engine must be running while bleeding. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Impulse | 1990-92 | LR, RR, RF, LF | Yes |  | Manual |  | Engine must be running while bleeding. If master cylinder requires bleeding, bleed it first. Remove ABS main fuse before bleeding system. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Impulse | 1990-92 | LR, RR, RF, LF | No |  | Manual |  | Engine must be running while bleeding. If master cylinder requires bleeding, bleed it first. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Oasis | 1996-97 | RR, LF, LR, RF | Yes |  | Either |  | If modulator requires bleeding, see service manual for special procedure. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Oasis | 1996-97 | RR, LF, LR, RF | No |  | Either |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Oasis | 1998-99 | LF, RF, RR, LR |  |  | Manual |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Pickup | 1984-85 | RR, LR, RF, LF |  | Rear | Manual |  | Engine must be running while bleeding. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Pickup | 1986-87 | LR, RR, LF, RF |  | Rear | Manual |  | Engine must be running while bleeding. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Stylus | 1991-92 | LR, RR, RF, LF |  |  | Manual |  | Engine must be running while bleeding. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Stylus | 1993 | LF, RR, RF, LR |  |  | Manual |  | Engine must be running while bleeding. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Trooper & Trooper II w/Rear ABS | 1984-95 | RR, LR, ALV, RF, LF | Yes | Rear | Manual |  | Engine must be running while bleeding to prevent damage to booster. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Trooper & Trooper II w/o Rear ABS | 1984-95 | RR, LR, RF, LF | No | Rear | Manual |  | Engine must be running while bleeding to prevent damage to booster. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Trooper & Trooper II w/4-Wheel ABS | 1995-99 | RR, LR, RF, LF | Yes | Rear |  |  | See service manual for special procedure. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| All Other Models | 1976-83 | LF, RF, LR, RR |  |  | Manual |  | Engine must be running while bleeding. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Jaguar |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| w/o ABS | 1976-85 | LR, RR, RF, LF | No | Rear |  |  | Engine must be running while bleeding to prevent damage to servo. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| w/o ABS | 1986-89 | RR, LR, RF, LF | No | Rear | Manual |  | DOT 4 brake fluid is required. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| w/ABS | 1986-94 | RF, LF, RR, LR | Yes | Rear |  |  | DOT 4 brake fluid is required. Front brakes must be manually bled. Accumulator must be discharged before bleeding. Key off, pump pedal at least 20 times until solid. Allow 3 second intervals between pedal strokes. Pedal must be released slowly. To bleed rear brakes, accumulator must be discharged. RR bleeder is opened first, hold pedal down, and key on. Wait at least 15 seconds to allow fluid to flow clear, then close bleeder. Slowly release pedal and key off. Repeat for LR. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| w/ABS | 1995-99 | RF, LF, RR, LR | Yes | Rear | Manual |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| KIA |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Sephia | 1994-96 | RR, LF, LR, RF | No | Front | Either | 10-30 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Sephia | 1995-97 | RR, LF, LR, RF | Yes | Front |  |  | In order to bleed system, the ABS Harness Adapter (OTC-3225) is required. See service manual for special procedure. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Sephia | 1998-99 | RF, LF, RR, LR | Yes | Front | Manual |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Sephia | 1998-99 | RF, LF, RR, LR | No | Front | Manual |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Sportage | 1995-96 | RR, LR, RF, LF |  | Rear | Manual |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Land Rover |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Discovery | 1997-99 |  |  | Rear | Manual |  | Battery must be disconnected while bleeding. Start at any caliper and procede in any order. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Range Rover | 1997-99 | LF, RF, LR, RR |  | Rear |  |  | See service manual for special procedure. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Lexus |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| All Models w/Traction Control |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| (Except LX470 & RX300) | 1990-99 | RR, LR, RF, LF |  |  | Manual |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| ES300 | 1997-98 | RR, LR, RF, LF |  |  | Manual |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| ES300 w/Traction Control | 1999 | RR, LR, RF, LF |  |  | Manual |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| ES300 w/Vehicle Skid Control | 1999 | RR, LR, RF, LF |  |  |  |  | See service manual for special procedure. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| GS300 & GS400 w/Traction Control | 1995-97 | RR, LR, RF, LF |  |  |  |  | See service manual for special procedure. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| GS300 & GS400 w/Hydaulic Booster | 1998-99 | RR, LR, RF, LF |  |  | Manual |  | See service manual for special procedure if reservoir runs dry, or hydraulic brake booster has been disassembled or replaced. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| LS400 w/Traction Control | 1995-99 | RR, LR, RF, LF |  |  | Manual |  | See service manual for special procedure if master cylinder runs dry or ABS/TRAC actuator is disassembled or replaced. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| LX470 | 1998-99 | RR, LR, RF, LF |  |  | Manual |  | See service manual for special procedure if reservoir runs dry, or hydraulic brake booster has been disassembled or replaced. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| RX300 | 1999 | RR, LR, RF, LF |  |  | Manual |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| SC300 & SC400 W/Traction Control | 1995-99 | RR, LR, RF, LF |  |  |  |  | See service manual for special procedure. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Mazda |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| B2000/2200/2600/2600i Pickup w/o ABS | 1986-89 | LR, RF, LF | No | Rear |  | 10-15 | Both rear wheels are controlled with LR bleeder. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| B2000/2200/2600/2600i Pickup w/RABS | 1990-94 | LR, HU, RF, LF | Yes | Rear |  | 10-15 | HU must be bled before bleeding fronts. Both rear wheels are controlled with LR bleeder. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| B2300/2500/3000/4000 Pickup w/o ABS | 1994-99 | RR, LR, RF, LF | No | Rear | Either |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| B2300/2500/3000/4000 Pickup w/RABS | 1994-97 | HU, RR, LR, RF, LF | Yes | Rear | Manual |  | ABS hydraulic unit must be bled first (located in engine compartment on left frame rail). If master cylinder has run dry or has been replaced, bleed it next. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| B2300/2500/3000/4000 Pickup w/4WABS | 1995-97 | HU, RR, LR, RF, LF | Yes | Rear |  |  | Special adapter is required to bleed master cylinder and hydraulic control unit (HCU) which must be bled before wheels. See service manual for procedure. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| B2300/2500/3000/4000 Pickup w/4WABS | 1998-99 | RR, LR, RF, LF | Yes | Rear | Manual |  | See service manual for special bleeding procedure if Hydraulic Control Unit (HCU) brakelines have been disconnected or if HCU has been replaced. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| GLC | 1981-85 | RF, LR, RR, LF |  | Front | Manual | 10-15 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| MPV w/o ABS | 1989 | RR, LR, RF, LF | No | Front | Manual | 10-15 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| MPV w/Rear Wheel ABS | 1990-95 | LR, HU, RF, LF | Yes | Front |  | 10-15 | Before bleeding front wheels, Hydraulic Unit (HU) (located above RR wheel) must be bled first. Both rear wheels are controlled by LR bleeder. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| MPV w4-Wheel ABS | 1996-98 |  | Yes | Front | Manual |  | Bleed starting with the longest brakeline. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Navajo | 1991-92 | RR, LR, RF, LF |  | Rear | Either | 10-30 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Navajo | 1993-94 | RR, LF, LR, RF |  | Rear |  | 10-30 | HCU and master cylinder must be bled before wheels. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| MX-6, Millenia, Miata, & 626 | 1996-99 |  |  | Front | Manual |  | Bleed starting with the longest brakeline. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Protégé | 1990-95 | RR, LR, LF, RF |  | Front | Either | 10-15 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Protégé | 1996-99 |  |  | Front | Manual |  | Bleed starting with the longest brakeline. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| RX7 | 1986-91 | RR, LR, RF, LF |  | Rear |  | 10-15 | The upper bleeder is the only one needed if rear caliper has not been disassembled. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| All Others | 1971-95 | RR, LR, RF, LF |  |  | Either | 10-15 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Mercedes-Benz |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| w/o ABS | 1974-85 | RR, LR, RF, LF | No | Rear | Either | 10-15 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| w/o ABS | 1988-89 |  | No | Rear | Either | 10-15 | Bleed starting with the longest brakeline. On 4-piston calipers, bleed both inside and outside bleeders. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| w/o ABS | 1990-92 |  | No | Rear |  |  | Bleed starting with the longest brakeline. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| w/ABS | 1979-95 |  | Yes | Rear |  |  | Bleed starting with the longest brakeline. Hydraulic unit screw labeled "SP" must be opened and bled until fluid runs clear after brakes have been bled on vehicles equipped with traction control. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| w/ABS | 1996-99 | RR, LR, RF, LF | Yes | Rear |  |  | See service manual for special procedure. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Mitsubishi |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Cordia & Tredia | 1983-85 | LR, RF, RR, LF |  |  | Either | 10-15 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Diamante, Eclipse, & 3000 GT w/o ABS | 1990-99 | RR, LF, LR, RF | No |  | Manual |  | Engine must be running when bleeding brakes. If master cylinder requires bleeding, bleed first. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Diamante, Eclipse, & 3000 GT w/ABS | 1990-99 | RR, LF, LR, RF | Yes |  | Manual |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Expo | 1991-95 | LR, RF, RR, LF |  |  | Manual |  | Engine must be running when bleeding brakes. If master cylinder requires bleeding, bleed first. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Galant 2WD w/ABS | 1983-92 |  | Yes |  |  |  | See service manual for special procedure. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Galant 4WD w/ABS | 1990-92 |  | Yes | 4WD |  |  | See service manual for special procedure. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Galant | 1993-99 | RR, LF, LR, RF |  |  |  |  | Engine must be running when bleeding brakes. If master cylinder requires bleeding, bleed first. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Mirage | 1989-94 | LR, RF, RR, LF |  |  |  |  | Engine must be running when bleeding brakes. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Mirage | 1995-99 | RR, LF, LR, RF |  |  | Manual |  | Engine must be running when bleeding brakes. If master cylinder requires bleeding, bleed first. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Montero | 1987-91 | RR, RF, LF |  | Rear |  | 10-15 | Both rear wheels are controlled by RR bleeder. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Montero | 1992-99 | RR, LR, LSPV, RF, LF | Yes | Rear | Manual | 10-15 | Engine must be running when bleeding brakes. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Montero | 1992-99 | RR, LR, LSPV, RF, LF | No | Rear |  | 10-15 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Montero & 2WD Truck | 1986 | RR, LR, RF, LF |  | Rear | Either | 10-15 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Montero Sport | 1997-99 | RR, LR, RF, LF | Yes | Rear | Manual |  | Engine must be running when bleeding brakes. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Montero Sport | 1997-99 | RR, LR, RF, LF | No | Rear |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Precis | 1988-94 | LR, RF, RR, LF |  |  | Either | 10-15 | Brake pedal must not be depressed when pressure bleeding. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Starion | 1986-89 | RR, LR, RF, LF |  |  |  | 10-15 | If equipped with hydraulic modulator, bleed before front brakes. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Van/Wagon & Truck | 1986-92 | RR, LSPV, RF, LF |  |  |  | 10-15 | LR is bled by Load Sensing Proportioning Valve (LSPV). |  |  |  |  |  |  |  |  |  |  |  |  |  |
| All Others | 1983-85 | RR, LR, RF, LF |  |  |  | 10-15 | Fluid level must be checked frequently. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| All Others | 1986-89 | LF, RF, RR, LR |  |  |  | 10-15 | Engine must be running while bleeding brakes on model year 1989 Galant and Mirage. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Nissan |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Altima | 1993-99 | RR, LF, LR, RF | Yes | Front | Manual |  | ABS actuator connectors must be disconnected or disconnect the battery before bleeding. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Altima | 1993-99 | RR, LF, LR, RF | No | Front |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Axxess | 1990 | LR, RF, RR, LF |  |  | Either | 10-15 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| B210 & 1200 | 1971-81 | LR, RR, LF, RF |  |  |  | 10-15 | Master cylinder lines must be bled first. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Frontier | 1998-99 | LR, RR, LF, RF | Yes | Rear |  |  | Disconnect battery or ABS actuator for 2WD models or electric unit on 4WD models. If equipped with load sensing proportioning valve bleed first, next bleed brakes, and last bleed ABS actuator on 2WD models or ABS actuator and electric unit on 4WD models. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Maxima | 1984-85 | RR, LR, RF, LF |  | Front |  | 10-15 | Fluid level must be checked frequently. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Maxima | 1986-94 | LR, RF, RR, LF | Yes | Front |  | 10-15 | If equipped with load sensing propotioning valve, bleed before rear wheels. Before bleeding, hydraulic actuator electrical connector must be disconnected. After bleeding wheels bleed front side of actuator followed by rear side. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Maxima | 1986-94 | LR, RF, RR, LF | No | Front |  | 10-15 | If equipped with load sensing propotioning valve, bleed before rear wheels. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Maxima | 1995-99 | RR, LF, LR, RF | Yes | Front | Manual |  | ABS actuator connectors must be disconnected or disconnect the battery before bleeding. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Maxima | 1995-99 | RR, LF, LR, RF | No | Front |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Quest | 1993-99 | RR, LF, LR, RF | No | Front | Manual |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Quest | 1993-99 | LF, RF, LR, RR | Yes | Front | Manual |  | ABS actuator connectors must be disconnected or disconnect the battery before bleeding. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Sentra, Pulsar/NX | 1986 | LR, RF, RR, LF |  | Front |  | 10-15 | Allow 20 second intervals between pedal strokes when bleeding secondary bore (front outlet) of master cylinder and LR and RF wheels. Allow 5 second intervals between strokes when bleeding primary bore (rear). |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Sentra, Pulsar/NX | 1987-94 | LR, RF, RR, LF | Yes | Front |  | 10-15 | Allow 5 second intervals between pedal strokes when bleeding master cylinder manually. Hydraulic actuator connector must be disconected before bleeding. After bleeding wheels, bleed front side of actuator followed by rear side. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Sentra, Pulsar/NX | 1987-94 | LR, RF, RR, LF | No | Front |  | 10-15 | Allow 5 second intervals between pedal strokes when bleeding master cylinder manually. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Sentra, Pulsar/NX | 1995-99 | RR, LF, LR, RF | Yes | Front | Manual |  | ABS actuator connectors must be disconnected or disconnect the battery before bleeding. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Sentra, Pulsar/NX | 1995-99 | RR, LF, LR, RF | No | Front |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Stanza, Stanza Wagon | 1986-92 | LR, RF, RR, LF | Yes | Front |  |  | Wheel cylinders must be bled after load sensing proportioning valve. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Stanza, Stanza Wagon | 1986-92 | LR, RF, RR, LF | No | Front |  |  | Wheel cylinders must be bled after load sensing proportioning valve. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Pickup & Pathfinder w/o ABS | 1980-99 | LR, RR, LF, RF | No | Rear |  | 10-15 | If vehicle is equipped with a load sensing proportioning valve, it must be bled first. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Pickup & Pathfinder w/Rear Wheel ABS | 1991-97 | LR, RR, LF, RF | Yes | Rear |  |  | If vehicle is equipped with a load sensing proportioning valve, it must be bled first. Next bleed wheel brakes, and finally bleed the ABS actuator. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Pickup & Pathfinder w/4-Wheel ABS | 1996-99 | LR, RR, LF, RF |  | Rear |  |  | ABS actuator must be disconnected or disconnect the battery before bleeding. If vehicle is equipped with load sensing proportioning valve, it must be bled first. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Van | 1987-88 | LR, RR, LF, RF |  |  | Either | 10-15 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 200SX, 240SX, 300ZX | 1984-89 | LR, RR, RF, LF |  |  | Either | 10-15 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 200SX | 1995-98 | RR, LF, LR, RF | Yes | Front | Manual |  | ABS actuator connectors must be disconnected or disconnect the battery before bleeding. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 200SX | 1995-98 | RR, LF, LR, RF | No | Front |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 240SX | 1990-94 | LR, RR, LF, RF | Yes | Front |  |  | ABS actuator connectors must be disconnected or disconnect the battery before bleeding. Next bleed wheel brakes followed by front then rear side of the actuator. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 240SX | 1990-94 | LR, RR, LF, RF | No | Front |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 240SX | 1995-96 | RR, LR, RF, LF | Yes | Front | Manual |  | ABS actuator connectors must be disconnected or disconnect the battery before bleeding. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 240SX | 1995-96 | RR, LR, RF, LF | No | Front |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 300ZX | 1990-94 | LR, RR, LF, RF | Yes | Rear |  |  | ABS actuator connectors must be disconnected or disconnect the battery before bleeding. Next bleed wheel brakes followed by front then rear side of the actuator. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 300ZX | 1990-94 | LR, RR, LF, RF | No | Rear |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 300ZX | 1995-96 | LR, RF, LF | Yes | Rear |  |  | ABS actuator connectors must be disconnected or disconnect the battery before bleeding. Next bleed wheel brakes followed by front then rear side of the actuator. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 300ZX | 1995-96 | LR, RF, LF | No | Rear |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 310 | 1979-82 | LR, RF, RR, LF |  |  |  | 10-15 | Master cylinder lines must be bled first. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| All Other RWD Cars | 1965-85 | RR, LR, RF, LF |  | Rear |  | 10-15 | Master cylinder lines must be bled first. Allow 5 second intervals between pedal strokes on Pulsar and Sentra models. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| All Other FWD Cars | 1976-85 | RR, LF, LR, RF |  | Front |  | 10-15 | Fluid level must be checked frequently. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Peugeot |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 405 & 505 | 1986-92 | RR, LR, RF, LF | No |  |  | 10-15 | Weight must be on vehicle's wheels while bleeding. Recommended method of bleeding is by pressure. All weels must be bled at the same time, close bleeders in sequence. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| All Others | 1965-85 | RR, LR, RF, LF | No |  |  | 10-15 | All wheels must be bled at the same time if pressure bleeding. If vehicle is equipped with rear disc brakes, pistons must be collapsed into caliper before bleeding. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 405 & 505 | 1986-92 | RR, LR, RF, LF | Yes |  |  | 10-15 | Weight must be on vehicle's wheels while bleeding. With key off, pump pedal 25 times to release system pressure. Fronts should be bled first, then bleed rears one at a time. Turn key on with pedal depressed. Close bleeder after fluid is key, then turn key off. Before repeating steps for other rear wheel, system must be depressurized again. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Porsche |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| All Models | 1965-85 | LR, RR, RF, LF |  | Rear |  | 10-15 | Outer caliper bleeder must be bled first if vehicle is equipped with both inner and outer. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| All Models | 1986-92 | LR, RR, RF, LF | Yes | Rear |  | 10-15 | ABS tester is required to bleed ABS portion of system. Normal methods can be used to bleed conventional part of the system. Outer bleeder m ust be bled first on vehicles equipped with both inner and outer bleeders. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Boxter w/ABS | 1997-99 | RR, LR, RF, LF | Yes | Rear |  | 22 | Fluid life is 2 years, DOT 4 is required. Recommended method of bleeding is by pressure. Use short pedal strokes when manual bleeding high milage vehicles to prevent damage to master cylinder primary cup. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Boxter w/ABS & Traction Control | 1997-99 | RR, LR, RF, LF | Yes | Rear |  | 22-29 | Fluid life is 2 years, DOT 4 is required. Recommended method of bleeding is by pressure. Use short pedal strokes when manual bleeding high milage vehicles to prevent damage to master cylinder primary cup. Use this procedure if hydraulic unit is removed or replaced. Pressure bleeder must be connected to master cylinder, Porsche Tester 2 must be connected to the Data Link Connector in the driver's footwell. Key on, then open the bleeder valve on RR. Choose ABS bleed option on tester. On tester choose START. System must be bled until fluid is free of air bubbles. Now close the bleeder and stop the bleed option. Key off then disconnect tester. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 911 2WD | 1993-94 |  |  | Rear |  | 29 | DOT 4 brake fluid is required. Master cylinder must be bled before wheels. Next bleed both caliper bleed screws, with them open pump pedal all the way down and up at least 4 times. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 911 All-Wheel Drive | 1993-94 |  |  | Rear |  | 22 | DOT 4 brake fluid is required. Bleed clutch hydraulics and master cylinder and change fluid. Bleed Icok cylinder and pressure lines and change brake fluid. Bleed lock and booster circuits and change fluid. To remove fluid at lock cylinders and operate solenoid valve, use Porsce Tester (9288). |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 911 w/ABS | 1995-96 | RR, LR, RF, LF | Yes | Rear |  |  | Fluid life is 2 years, DOT 4 is required. Use short pedal strokes when manual bleeding high milage vehicles to prevent damage to master cylinder primary cup. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 911 w/ABS & Traction Control | 1995-99 | RR, LR, RF, LF | Yes | Rear |  | 22-29 | Fluid life is 2 years, DOT 4 is required. Use short pedal strokes when manual bleeding high milage vehicles to prevent damage to master cylinder primary cup. Use this procedure if hydraulic unit is removed or replaced. Pressure bleeder must be connected to master cylinder, Porsche Tester 2 must be connected to the Data Link Connector in the driver's footwell. Key on, then open the bleeder valve on RR. Choose ABS bleed option on tester. On tester choose START. System must be bled until fluid is free of air bubbles. Now close the bleeder and stop the bleed option. Key off then disconnect tester. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Renault |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Medallion | 1987-89 | LR, RR, RF, LF |  |  |  | 10-15 | Engine must be off while bleeding. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| R-5, R-8, R-10, R-12, R-15, R-16, & R-17 | 1969-80 | LF, RF, LR, RR |  |  |  | 10-15 | Fluid level must be checked frequently. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| All Others | 1981-88 | RR, LF, LR, RF |  |  | Manual | 10-15 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| All Others | 1981-88 | RR, LR, RF, LF |  |  | Pressure | 10-15 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| SAAB |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 900, 99, Sonnett II | 1970-89 | LR, RF, RR, LF |  |  |  | 10-15 | Fluid level must be checked frequently. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 9000 | 1986-89 | RR, LR, LF, RF |  |  |  | 10-15 | DOT 4 brake fluid is required. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 9000, 900 | 1990-92 | LR, RF, RR, LF |  |  | Either | 10-15 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 900 & 9000 | 1990-92 | RR, LR, RF, LF |  |  |  | 10-15 | System must be free of pressure. Key off and pump pedal 20 times. Fronts must be bled fled first by normal method. Rears must be bled one at a time. While depressing pedal, key on. Close bleeder after fluid is clear. Key off and release system pressure again. Repeat process on other rear. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 900 | 1993-96 | RF, LF, LR, RR |  |  |  | 10-15 | System must be free of pressure. Key off and pump pedal 20 times. Fronts must be bled fled first by normal method. Rears must be bled one at a time. While depressing pedal, key on. Close bleeder after fluid is clear. Key off and release system pressure again. Repeat process on other rear. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 900 | 1997-98 | LF, RF, LR, RR |  |  | Either |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 9000 | 1993-94 | RF, LF, LR, RR |  |  |  |  | System must be free of pressure. Key off and pump pedal 20 times. Fronts must be bled fled first by normal method. Rears must be bled one at a time. While depressing pedal, key on. Close bleeder after fluid is clear. Key off and release system pressure again. Repeat process on other rear. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 9000 (Mark IV ABS) | 1995-96 | RF, LR, LF, RR |  |  |  |  | Breakout Box (86-11-06), Breakout Box Lead (86-11-006), and Jumper Harness (86-11-212) is required for bleeding. See service manual for special procedure. Dot 4 brake fluid is required. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 9-3 & 9-5 | 1999 | LF, RR, RF, LR |  |  | Vacuum |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Sterling |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| All Models | 1986-89 | LF, RR, RF, LR |  |  |  | 10-15 | Fluid level must be checked frequently. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Subaru |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Justy | 1987-89 | RR, LR, RF, LF |  |  |  | 10-15 | Fluid level must be checked frequently. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Justy | 1990-94 |  |  |  |  | 10-15 | Longest line must be bled first. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Forester | 1998-99 | RF, LR, LF, RR |  |  |  |  | See service manual for special bleeding procedure. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Impreza, Outback, & Legacy w/o ABS | 1990-99 | RF, LR, LF, RR |  |  |  | 10-15 | Allow 3-4 second intervals between pedal strokes when manually bleeding. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Impreza, Outback, & Legacy w/ABS Only | 1990-94 | HU, RF, LR, HU, LF, RR |  |  |  | 10-15 | Before bleeding RF and LR, bleed secondary hydraulic unit bleeder. Before bleeding LF and RR, bleed primary hydraulic unit bleeder. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Impreza, Outback, & Legacy w/ABS Only | 1995-97 | RF, LR, LF, RR |  |  |  |  | Allow 3-4 second intervals between pedal strokes when manually bleeding. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Impreza, Outback, & Legacy w/ABS Only | 1998-99 | RF, LR, LF, RR |  |  |  |  | See service manual for special bleeding procedure. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Legacy w/ABS & Traction Control | 1995-97 | RF, LR, LF, RR |  |  |  |  | See service manual for special bleeding procedure. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Loyale, XT, XT6 | 1990-94 | LF, RR, RF, LR |  |  |  | 10-15 | Primary and secondary hydraulic unit must be bled before bleeding wheels. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| SVX | 1992-97 | HU, HU, RF, LR, LF, RR |  |  |  | 10-15 | Master cylinder lines must be bled first. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| All Others | 1980-85 | LR, RF, RR, LF |  |  |  | 10-15 | Fluid level must be checked frequently. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| All Others | 1986-89 | LF, RR, RF, LR |  |  |  | 10-15 | Fluid level must be checked frequently. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Suzuki |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Esteem | 1995-99 | RR, LF, LR, RF |  |  | Manual |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Grand Vitara | 1999 | LR, LSPV, RF, LF |  |  |  |  | RR bleeding is controlled by Load Sensing Proportioning Valve (LSPV). |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Grand Vitara | 1999 | LR, RF, LF |  |  | Manual |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Samurai | 1986-87 | RR, LF, LR, RF |  |  |  | 10-15 | Fluid level must be checked frequently. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Samurai | 1988-92 | LR, LSPV, RF, LF |  |  |  | 10-15 | RR bleeding is controlled by Load Sensing Proportioning Valve (LSPV). |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Samurai | 1993-94 | RF, LF, LSPV, LR |  |  |  | 31-24 | RR bleeding is controlled by Load Sensing Proportioning Valve (LSPV). |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Sidekick & X-90 w/o ABS | 1989-92 | LR, LSPV, RF, LF |  |  |  | 10-15 | RR bleeding is controlled by Load Sensing Proportioning Valve (LSPV). |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Sidekick & X-90 w/o ABS | 1993-98 | RF, LF, LSPV, LR |  |  |  |  | RR bleeding is controlled by Load Sensing Proportioning Valve (LSPV). |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Sidekick & X-90 w/ABS | 1991-95 | RF, LF, LR |  |  |  | 10-15 | After wheels have been bled, bleed pressure limit valve. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Sidekick & X-90 w/Delco VI ABS (1.6L) | 1996-99 | LR, RF, LF |  |  |  |  | Tech-2 is required to place displacement pistons in upper position. See service manual for procedure. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Sidekick Sport | 1996-98 | RF, LF, LR |  |  | Manual |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Swift w/o ABS | 1989-99 | RR, LF, LR, RF |  |  |  | 10-15 | Fluid level must be checked frequently. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Swift w/Delco VI ABS | 1995-99 | RR, LR, RF, LF |  |  |  |  | Tech-2 is required to place displacement pistons in upper position. See service manual for procedure. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Vitara w/o ABS | 1999 | LR, LSPV, RF, LF |  |  |  |  | RR bleeding is controlled by Load Sensing Proportioning Valve (LSPV). |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Vitara w/ABS | 1999 | LR, RF, LF |  |  | Manual | 35 | See service manual for procedure if standard bleeding does not remove all air or if ABS actuator is replaced. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Toyota |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Corolla w/ABS | 1998-99 |  |  |  |  |  | Longest line must be bled first and shortest line must be bled last. See service manual for special bleeding procedure for ABS actuator. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Land Cruiser | 1998-99 |  |  |  | Manual |  | See service manual for special procedure if hydraulic brake booster has been disassembled or replaced. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Pickup & 4Runner w/Rear ABS | 1990-95 |  |  |  |  |  | Longest line must be bled first and shortest line must be bled last. See service manual for special bleeding procedure for Rear Anti-Lock System (RABS). |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Supra W/Traction Control | 1995-98 |  |  |  |  |  | Longest line must be bled first and shortest line must be bled last. See service manual for special bleeding procedure for TRAC system if traction actuator or master cylinder is removed. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| All Other Models | 1965-99 |  |  |  |  | 10 | Longest line must be bled first and shortest line must be bled last. After bleeding wheel cylinders, bleed by-pass valve and load sensing proportioning valve. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Volkswagen |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Dasher | 1974-81 | RR, LR, RF, LF |  |  |  | 10-15 | When bleeding brake pressure regulator lever must be pushed toward rear axle. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Vanagon & Type II | 1975-89 | RR, LR, RF, LF |  |  |  | 10-15 | Fluid level must be checked frequently. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| All Others | 1979-81 | RR, LR, RF, LF |  |  |  | 10-15 | If vehicle is equipped with booster, disconnect vacuum hose and check valve before bleeding. When bleeding, brake pressure regulator lever must be pushed toward rear axle. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| All Others | 1982-96 | RR, LR, RF, LF |  |  |  | 10-15 | DOT 4 brake fluid is required. If vehicle is equipped with booster, disconnect vacuum hose and check valve before bleeding. Brake pressure regulator lever must be pushed toward rear axle while bleeding. Bleed pressure regulator first on Quantum Synchro. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| All Others w/ABS | 1990-94 | LF, RF, RR, LR |  |  |  | 10-15 | DOT 4 brake fluid is required. System must be free of pressure. With key off, brake pedal must be depressed at least 20 times. Front brakes may be bled using normal manual or pressure methods. Rear brakes must have system free of pressure. Open bleeder screw after connecting bleeder hose. Key on, until fluid flows clear, press regulator level towards the rear axle. Finally close the bleeder and relieve system of pressure. Repeat procedure for other rear wheel. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| All Others w/ABS | 1995-97 | RR, LR, RF, LF |  |  |  |  | DOT 4 brake fluid is required. If vehicle is equipped with booster, disconnect vacuum hose and check valve before bleeding. Brake pressure regulator lever must be pushed toward rear axle while bleeding. Bleed pressure regulator first on Quantum Synchro. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Beetle, Golf, & Jetta | 1998-99 | RR, LR, RF, LF |  |  | Either | 14 | DOT 4 brake fluid is required. Fluid level must be checked frequently. ABS must be bled using VW scan tool (VAG 1551) if ABS hydraulic unit runs dry or is replaced. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Passat | 1998-99 | RR, LR, RF, LF |  |  | Either | 14 | DOT 4 brake fluid is required. Fluid level must be checked frequently. If vehicle is equipped with rear brake pressure regulator, move lever toward rear wheels when bleeding rear wheels. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Volvo |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 240, 260, 740, & 760 | 1975-85 | LF, RF, LR, RR | No |  |  | 10-15 | Rear of vehicle must be higher than front. All 3 front caliper bleeders must be bled at same time. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 240 | 1986-92 | LF, RF, LR, RR | No |  |  | 10-15 | Fluid level must be checked frequently. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 740, 760, 940, & 960 | 1986-92 | RR, LR, RF, LF | No |  |  | 10-15 | Fluid level must be checked frequently. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 740, 760, & 780 | 1987 | LF, RF, LR, RR | Yes |  |  | 10-15 | Bleed both bleeders at same time if calipers are equipped with 2. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 240, 740, 760, 780, 850, 940, & 960 | 1988-97 | LR, RR, LF, RF | Yes |  |  | 10-15 | Bleed both bleeders at same time if calipers are equipped with 2. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| S90 & V90 | 1998-99 | LR, RR, LF, RF | Yes |  | Manual |  | DOT 4 brake fluid is required. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 850, C70, S70, & V70 w/ABS & TCS | 1997-99 | LF, RF, LR, RR | Yes |  |  |  | Dot 4 brake fluid is required. Shut engine off and depress pedal 3-4 times, 1.6 inches (40.6mm) is the limit of travel. If pedal travel exceeds specifications, bleed again and recheck travel. |  |  |  |  |  |  |  |  |  |  |  |  |  |

© Copyright 2016 by James Halderman