## Slide 1: Automotive Engines Theory and Servicing
Ninth Edition
Chapter 11
Diesel Engine Operation and Diagnosis

## Slide 2: OBJECTIVES (1 OF 3)
11.1 State the characteristics of diesel engines.
11.2 Describe the fuel tank and lift pump, injection pump, and engine-driven vacuum pump.
11.3 Explain the HEUI system.
11.4 Discuss the purpose of glow plugs, diesel fuel heaters, diesel injector nozzles, and accelerator pedal position sensors.

## Slide 3: OBJECTIVES (2 OF 3)
11.5 Explain the purpose of diesel engine turbochargers.
11.6 Discuss the purpose of the exhaust gas recirculation system, selective catalytic reduction, and diesel oxidation catalysts.
11.7 Explain diesel particulate matter, and discuss the function of diesel exhaust particulate filters.

## Slide 4: OBJECTIVES (3 OF 3)
11.8 Discuss diesel exhaust smoke diagnosis.
11.9 Discuss compression testing, glow plug resistance balance test, injector pop testing, and diesel emission testing.

## Slide 5: DIESEL ENGINES (1 OF 3)
The diesel engine uses heat created by compression to ignite the fuel, so it requires no spark ignition system.
  The diesel engine requires compression ratios of 16:1 and higher.
  Incoming air is compressed until its temperature reaches about 1,000°F (540°C).
  This is called heat of compression.

## Slide 6: DIESEL ENGINES (2 OF 3)
As the piston reaches the top of its compression stroke, fuel is injected into the cylinder, where it is ignited by the hot air.
As the fuel burns, it expands and produces power.
  It is made heavier and stronger than the same size gasoline-powered engine.

## Slide 7: DIESEL ENGINES (3 OF 3)
A diesel engine uses a fuel system with a precision injection pump and individual fuel injectors.
  The pump delivers fuel to the injectors at a high pressure and at timed intervals.
  Each injector sprays fuel into the combustion chamber at the precise moment required for efficient combustion.

## Slide 8: FIGURE 11–1 Diesel combustion occurs when fuel is injected into the hot, highly compressed air in the cylinder.

## Slide 9: FIGURE 11–2 A Typical high-pressure common rail (HPCR) type diesel fuel system.

## Slide 10: THREE PHASES OF COMBUSTION
What are the three phases to the combustion in a diesel engine?

## Slide 11: FUEL TANK AND LIFT PUMP PARTS INVOLVED
A fuel tank used on a vehicle equipped with a diesel engine differs from the one used with a gasoline engine.
  The filler neck is larger for diesel fuel.
  There are no evaporative emission control devices or a charcoal (carbon) canister.
FIGURE 11–7 A fuel temperature sensor is being tested using an ice bath.

## Slide 12: INJECTION PUMP
Need For High-pressure Fuel Pump
Distributor Injection Pump
High-pressure Common Rail
FIGURE 11–8 A typical distributor-type diesel injection pump showing the pump, lines, and fuel filter.

## Slide 13: HEUI SYSTEM (1 OF 2)
The components used include:
  High-pressure engine oil pump and reservoir
  Pressure regulator for the engine oil
  Passages in the cylinder head for flow of fuel to the injectors

## Slide 14: HEUI SYSTEM (2 OF 2)
The engine oil is pressurized to provide an opening pressure strong enough to overcome the fuel pressure when the solenoid is commanded to open by the PCM.

## Slide 15: FIGURE 11–11 A HEUI injector from a Ford PowerStroke diesel engine. The O-ring grooves indicate the location of the O-rings that seal the fuel section of the injector from coolant and from the engine oil.

## Slide 16: DIESEL INJECTOR NOZZLES (1 OF 2)
The tip of the injector nozzle has many holes to deliver an atomized spray of diesel fuel into the cylinder.
The electric solenoid attached to the injector nozzle is computer controlled and opens to allow fuel to flow into the injector pressure chamber.

## Slide 17: DIESEL INJECTOR NOZZLES (2 OF 2)
Parts of a diesel injector nozzle include:
  Heat shield
  Injector body
  Diesel injector needle valve
  Injector pressure chamber

## Slide 18: FIGURE 11–12 Typical computer-controlled diesel engine fuel injectors.

## Slide 19: GLOW PLUGS
Purpose and Function
Operation
Heated Inlet Air
FIGURE 11–14 A glow plug assortment showing the various types and sizes of glow plugs used. Always use the specified glow plugs.

## Slide 20: ENGINE-DRIVEN VACUUM PUMP (1 OF 2)
Because a diesel engine is unthrottled, it creates very little vacuum in the intake manifold.
  Several engine and vehicle components operate using vacuum, such as the exhaust gas recirculation (EGR) valve and the heating and ventilation blend and air doors.

## Slide 21: ENGINE-DRIVEN VACUUM PUMP (2 OF 2)
  Most diesels used in cars and light trucks are equipped with an engine-driven vacuum pump to supply the vacuum for these components.

## Slide 22: DIESEL FUEL HEATERS
Diesel fuel heaters help prevent power loss and stalling in cold weather.
  The heater is placed in the fuel line between the tank and the primary filter.
  Some coolant heaters are thermostatically controlled, which allows fuel to bypass the heater once it has reached operating temperature.

## Slide 23: ACCELERATOR PEDAL POSITION SENSOR
Some light-truck diesel engines are equipped with an electronic throttle to control the amount of fuel injected into the engine.
A throttle-by-wire system uses an accelerator pedal position (APP) sensor.

## Slide 24: FIGURE 11–17 A typical accelerator pedal position (APP) sensor uses three different sensors in one package with each creating a different voltage as the accelerator is moved.

## Slide 25: DIESEL ENGINE TURBOCHARGERS
Turbocharged Diesels
Air Charge Cooler
Variable Turbocharger
FIGURE 11–18 A Cummins diesel turbocharger is used to increase the power and torque of the engine.

## Slide 26: EXHAUST GAS RECIRCULATION (1 OF 2)
The EGR system recycles some exhaust gas back into the intake stream to cool combustion, which reduces oxides of nitrogen (NOx) emissions.
The EGR system includes:
  Plumbing that carries some exhaust gas from the turbocharger exhaust inlet to the intake ports

## Slide 27: EXHAUST GAS RECIRCULATION (2 OF 2)
  EGR control valve
  Stainless steel cooling element used to cool the exhaust gases

## Slide 28: FIGURE 11–21 A cutaway showing the exhaust cooler. The cooler the exhaust is, the more effective it is in controlling NOx emissions.

## Slide 29: DIESEL PARTICULATE MATTER
Particulate Matter Standards
  Total suspended particulate (TSP)
  PM10
  PM2.5
Soot Categories
  Fine
  Ultrafine

## Slide 30: FIGURE 11–22 Relative size of particulate matter to a human hair.

## Slide 31: DIESEL OXIDATION CATALYST (1 OF 2)
Catalysts chemically react with exhaust gas to convert harmful nitrogen oxide into nitrogen dioxide, and to oxidize absorbed hydrocarbons.
The chemical reaction acts as a combustor for the unburned fuel that is characteristic of diesel compression ignition.

## Slide 32: DIESEL OXIDATION CATALYST (2 OF 2)
The DOC reduces: Carbon monoxide (CO), Hydrocarbons (HC), Odor-causing compounds such as aldehydes and sulfur.

## Slide 33: DIESEL EXHAUST PARTICULATE FILTER (1 OF 2)
Purpose and Function
Operation
Exhaust Gas Temperature Sensors
DPF Differential Pressure Sensor
Diesel Particulate Filter Regeneration

## Slide 34: DIESEL EXHAUST PARTICULATE FILTER (2 OF 2)
DPF Regeneration Process
Types of DPF Regeneration
Ash Loading

## Slide 35: FIGURE 11–24 Aftertreatment of diesel exhaust is handled by the DOC and DPF.

## Slide 36: SELECTIVE CATALYTIC REDUCTION
Purpose and Function
  Selective catalytic reduction (SCR) is a method used to reduce NOx emissions by injecting urea into the exhaust stream.
  Instead of using large amounts of exhaust gas recirculation (EGR), the SCR system uses a urea.
Advantages of SCR
Disadvantages of SCR

## Slide 37: FIGURE 11–30 Diesel exhaust fluid is housed in a separate container that holds from 5 to 10 gallons, or enough to last until the next scheduled oil change in most diesel vehicles that use SCR.

## Slide 38: DIESEL EXHAUST SMOKE DIAGNOSIS (1 OF 2)
Some exhaust smoke is considered normal operation for many diesel engines, especially older units.

## Slide 39: DIESEL EXHAUST SMOKE DIAGNOSIS (2 OF 2)
The cause of excessive exhaust smoke should be diagnosed and repaired.
  Black Smoke
  White Smoke
  Gray or Blue Smoke

## Slide 40: DISEL PERFORMANCE DIAGNOSIS
Common faults include:
  Hard starting
  No start
  Extended cranking before starting
  Low power

## Slide 41: FIGURE 11–32 A pressure gauge checking the fuel pressure from the lift pump on a Cummins 6.7 liter diesel.

## Slide 42: COMPRESSION TESTING (1 OF 2)
A compression test is fundamental for determining the mechanical condition of a diesel engine.
Worn piston rings can cause low power and excessive exhaust smoke.

## Slide 43: COMPRESSION TESTING (2 OF 2)
To test the compression on a diesel engine, the following will have to be done.
  Remove the glow plug (if equipped) or the injector.
  Use a diesel compression gauge, as the compression is too high to use a gasoline engine compression gauge.

## Slide 44: FIGURE 11–33 A compression gauge that is designed for the higher compression ratio of a diesel engine should be used when checking the compression.

## Slide 45: GLOW PLUG RESISTANCE BALANCE TEST
Glow plugs increase in resistance as their temperature increases.
All glow plugs should have about the same resistance when checked with an ohmmeter.
A similar test of the resistance of the glow plugs can be used to detect a weak cylinder.
This test is particularly helpful on a diesel engine that is not computer controlled.

## Slide 46: INJECTOR POP TESTING
A pop tester is a device used for checking a diesel injector nozzle for proper spray pattern.
The handle is depressed and popoff pressure is displayed on the gauge.
FIGURE 11–34 A typical pop tester used to check the spray pattern of a diesel engine injector.

## Slide 47: DIESEL EMISSION TESTING
Opacity Test
Snap Acceleration Test
Rolling Acceleration Test
Stall Acceleration Test

## Slide 48: SUMMARY (1 OF 3)
A diesel engine uses heat of compression to ignite the diesel fuel when it is injected into the compressed air in the combustion chamber.
The typical diesel engine fuel system consists of the fuel tank, lift pump, water-fuel separator, and fuel filter.

## Slide 49: SUMMARY (2 OF 3)
The engine-driven injection pump supplies high-pressure diesel fuel to the injectors.
Injector nozzles are either opened by the high-pressure pulse from the distributor pump or electrically by the computer on a common rail design.

## Slide 50: SUMMARY (3 OF 3)
Glow plugs are used to help start a cold diesel engine and help prevent excessive white smoke during warm-up.
Emissions are controlled on newer diesel engines
Diesel engine testing