## Slide 1: Automotive Engines Theory and Servicing
Ninth Edition
Chapter 17
Engine Starting and Charging Systems

## Slide 2: OBJECTIVES
17.1 Explain the purpose and function of a battery, and discuss battery ratings.
17.2 Discuss battery service and battery service safety considerations.
17.3 Discuss battery voltage test, battery load testing, and conductance testing.
17.4 Explain how to safely jump start a battery, and discuss battery charging and charging circuit.

## Slide 3: OBJECTIVES
17.5 Explain the battery electrical drain test.
17.6 Describe the cranking circuit, and discuss how to diagnose starter problems using visual inspection.
17.7 Explain starter testing on a vehicle and how to test a starter using a scan tool.
17.8 Discuss voltage drop testing and how to check charging system voltage.

## Slide 4: OBJECTIVES
17.9 Discuss the need for proper starter drive-to-flywheel clearance.
17.10 Discuss how to test an alternator using a scan tool and using a scope.
17.11 Discuss AC ripple voltage check and AC current check.
17.12 Explain charging system voltage drop testing and alternator output test.

## Slide 5: PURPOSE AND FUNCTION OF A BATTERY
An automotive battery provides a source of electrical power for starting and for electrical demands that exceed alternator output.
  The battery also acts as a voltage stabilizer for the entire electrical system.

## Slide 6: BATTERY RATINGS
Batteries are rated according to the amount of current they can produce under specific conditions.
  Cold-cranking Amperes
  Cranking Amperes
  Marine Cranking Amperes
  Ampere-hour Rating
  Reserve Capacity

## Slide 7: Figure 17–1 This battery shows a large “1000” on the front panel but this is the CA rating and not the more important CCA rating. Always compare batteries with the same rating.

## Slide 8: BATTERY SERVICE SAFETY CONSIDERATIONS (1 OF 2)
Batteries contain acid and release explosive gases (hydrogen and oxygen) during normal charging and discharging cycles.
To help prevent physical injury or damage to the vehicle, always adhere to the following safety procedures.
  Disconnect the negative battery cable from the battery.

## Slide 9: BATTERY SERVICE SAFETY CONSIDERATIONS (2 OF 2)
  Wear eye protection whenever working around any battery.
  Wear protective clothing to avoid skin contact with battery acid.
  Always adhere to all safety precautions as stated in the service procedures for the equipment used for battery service and testing.
  Never smoke or use an open flame around any battery.

## Slide 10: BATTERY VISUAL INSPECTION AND VOLTAGE TEST
The battery and battery cables should be included in the list of items checked during a thorough visual inspection.
Check the battery cables for corrosion and tightness
Testing the battery voltage with a voltmeter is a simple method for determining the state of charge of any battery.

## Slide 11: Figure 17–3 A visual inspection on this battery showed that the electrolyte level was below the plates in all cells.

## Slide 12: Figure 17–4 Using a DMM to measure the open-circuit voltage of a battery.

## Slide 13: BATTERY LOAD TESTING
What is a battery load test?
If the battery fails the load test, recharge the battery and retest.
If the battery fails the load test again, replace the battery.

## Slide 14: Figure 17–7 A Midtronics tester that can not only test the battery but can also detect faults with the starter and alternator.

## Slide 15: CONDUCTANCE TESTING
General Motors Corporation, Chrysler Corporation, Ford, and other vehicle manufacturers specify that a conductance tester be used to test batteries in vehicles still under factory warranty.
  It uses its internal electronic circuitry to determine the state of charge and capacity of the battery by measuring the voltage and conductance of the plates.

## Slide 16: Figure 17–9 An electronic battery tester.

## Slide 17: JUMP STARTING (1 OF 2)
To safely jump start a vehicle without doing any harm, use the following procedure.
  Be certain the ignition switch is off on both vehicles.
  Connect good-quality copper jumper cables.

## Slide 18: JUMP STARTING (2 OF 2)
  Start the vehicle with the good battery and allow it to run for 5 to 10 minutes. This allows the alternator of the good vehicle to charge the battery on the disabled vehicle.
  Start the disabled vehicle and, after the engine is operating smoothly, disconnect the jumper cables in the reverse order of step 2.

## Slide 19: Figure 17–10 Jumper cable usage guide. Follow the same connections if using a portable jump box.

## Slide 20: BATTERY CHARGING AND SERVICE (1 OF 2)
It is best to slow-charge any battery to prevent possible overheating damage to the battery.
Remember, it may take eight hours or more to charge a fully discharged battery.

## Slide 21: BATTERY CHARGING AND SERVICE (2 OF 2)
Check and service the following items if needed.
  Neutralize and clean any corrosion from the battery terminals with a solution of baking soda and water.
  Carefully inspect the battery cables by visual inspection.
  Check the tightness and cleanliness of all ground connections.

## Slide 22: Figure 17–11 To use a battery charger, make sure the charger is connected to the battery before plugging in the charger.

## Slide 23: Figure 17–12 This battery cable was found corroded underneath. The corrosion had eaten through the insulation yet was not noticeable without careful inspection. This cable should be replaced.

## Slide 24: BATTERY ELECTRICAL DRAIN TEST (1 OF 2)
The battery electrical drain test determines if some component or circuit in a vehicle or truck is causing a drain on the battery when everything is off.
  This test is also called the ignition off-draw (IOD) or parasitic load test.

## Slide 25: BATTERY ELECTRICAL DRAIN TEST (2 OF 2)
This test should be performed whenever one of the following conditions exists.
  Whenever a battery is being charged or replaced
  Whenever the battery is suspected of being drained

## Slide 26: BATTERY ELECTRICAL DRAIN TESTING USING AN AMMETER (1 OF 2)
The ammeter method is the most accurate way to test for a possible battery drain.
Connect an ammeter in series between the battery terminal (post) and the disconnected cable.
  Normal battery drain is 0.020 to 0.030 A and any drain greater than 0.050 A should be found and corrected.

## Slide 27: BATTERY ELECTRICAL DRAIN TESTING USING AN AMMETER (2 OF 2)
Many digital multimeters have an ammeter scale that can be used to safely and accurately test for an abnormal parasitic drain.

## Slide 28: PROCEDURE FOR BATTERY ELECTRICAL DRAIN TEST
What conditions should exist in order to perform this test?
Normal battery drain on a vehicle equipped with electronic radio, climate control, computerized fuel injection, and so forth,

## Slide 29: Figure 17–14 This mini clamp-on DMM is being used to measure the amount of battery electrical drain that is present. In this case, a reading of 20 mA (displayed on the meter as 00.02 A) is within the normal range of 20 to 30 mA. Be sure to clamp around all of the positive battery cables or all of the negative battery cables, whichever is easiest to clamp.

## Slide 30: FINDING THE SOURCE OF THE DRAIN
If there is a drain, check and temporarily disconnect the following components.
  1. Cell phone or MP3 player still connected to the vehicle
  2. Glove compartment light
  3. Trunk light

## Slide 31: WHEN A BATTERY DRAIN EXISTS AFTER FUSES ARE DISCONNECTED
What are the most common sources of drain under the hood?

## Slide 32: CRANKING CIRCUIT (1 OF 2)
The cranking circuit includes those mechanical and electrical components required to crank the engine for starting.
The cranking force in the early 1900s was the driver's arm.

## Slide 33: CRANKING CIRCUIT (2 OF 2)
Modern cranking circuits include the following:
  Starter motor
  Battery
  Starter solenoid or relay
  Starter drive
  Ignition switch

## Slide 34: Figure 17–17 A typical ignition switch showing all of the electrical terminals after the connector has been removed.

## Slide 35: DIAGNOSING STARTER PROBLEMS USING VISUAL INSPECTION (1 OF 2)
Carefully check the battery cables for tightness both at the battery and at the starter, and block connections.
Check to see if the heat shield (if equipped) is in place.

## Slide 36: DIAGNOSING STARTER PROBLEMS USING VISUAL INSPECTION (2 OF 2)
Check for any nonstock add-on accessories or equipment that may drain the battery such as a sound system or extra lighting.
Crank the engine.

## Slide 37: Figure 17–20 Carefully inspect all battery terminals for corrosion.

## Slide 38: STARTER TESTING ON THE VEHICLE (1 OF 2)
Check Battery
Starter Amperage Test
  Excessive current draw may indicate one or more of the following:
    Low battery voltage (discharged or defective battery)
    Binding of starter armature as a result of worn bushings

## Slide 39: STARTER TESTING ON THE VEHICLE (2 OF 2)
    Oil too thick (viscosity too high) for weather conditions
    Shorted or grounded starter windings or cables
    Tight or seized engine

## Slide 40: Figure 17–21 When connecting a starter tester such as a Sun VAT 45 to the vehicle, make certain that the inductive probe is placed over all of the cables or wires from the battery.

## Slide 41: TESTING A STARTER USING A SCAN TOOL (1 OF 2)
Connect the scan tool according to the manufacturer's instructions.
Select battery voltage and engine RPM on the scan tool.
Select "snapshot" and start recording or graphing if the scan tool is capable.

## Slide 42: TESTING A STARTER USING A SCAN TOOL (2 OF 2)
Crank the engine. Stop the scan tool recording.
Retrieve the scan data and record cranking RPM and battery voltage during cranking.

## Slide 43: VOLTAGE DROP TESTING AND DRIVE-TO-FLYWHEEL CLEARANCE
Purpose of Voltage Drop Testing
Results of Excessive Voltage Drop
Performing A Voltage Drop Test
Need For Proper Clearance
  There must be a slight clearance between the starter pinion and the engine flywheel ring gear.
Checking For Proper Clearance

## Slide 44: Figure 17–26 Starter diagnosis chart.

## Slide 45: Figure 17–27 A shim (or half shim) may be needed to provide the proper clearance between the flywheel teeth of the engine and the pinion teeth of the starter.

## Slide 46: CHARGING CIRCUIT (1 OF 2)
An alternator is constructed of a two-piece cast-aluminum housing.
  Aluminum is used because of its lightweight, nonmagnetic properties and heat transfer properties

## Slide 47: CHARGING CIRCUIT (2 OF 2)
  A front ball bearing is pressed into the front housing to provide the support and friction reduction necessary for the belt-driven rotor assembly.
  The rear housing usually contains a roller-bearing support for the rotor and mounting for the brushes, diodes, and internal voltage regulator

## Slide 48: Figure 17–28 Cutaway view of a typical AC alternator.

## Slide 49: CHECKING CHARGING SYSTEM VOLTAGE
Digital Multimeter Connections
Charging System Voltage Specifications
Charging System Voltage Test Procedure
FIGURE 17–29 The digital multimeter should be set to read DC volts and the red lead connected to the battery positive (+) terminal and the black meter lead connected to the negative (-) battery terminal.

## Slide 50: TESTING AN ALTERNATOR USING A SCAN TOOL (1 OF 2)
A scan tool can be used on most General Motors and Chrysler Corporation vehicles and others that have datastream information.
Follow these steps:
  Connect the scan tool according to the manufacturer's instructions.

## Slide 51: TESTING AN ALTERNATOR USING A SCAN TOOL (2 OF 2)
  Select battery voltage and engine RPM on the scan tool.
  Start the engine and operate at 2,000 RPM.
  Observe the battery voltage. This voltage should be between 13.5 and 15 volts (or within the manufacturer's specifications).

## Slide 52: AC RIPPLE VOLTAGE CHECK AND VOLTAGE DROP TESTING (1 OF 2)
Set the digital meter to read AC volts.
Start the engine and operate it at 2,000 RPM (fast idle).
Connect the voltmeter leads to the positive and negative battery terminals.

## Slide 53: AC RIPPLE VOLTAGE CHECK AND VOLTAGE DROP TESTING (2 OF 2)
Turn on the headlights to provide an electrical load on the alternator.
Purpose of Charging System Voltage Drop Testing
Charging System Voltage Drop Testing Procedure

## Slide 54: AC CURRENT CHECK
The amount of AC current (also called ripple current) in amperes flowing from the alternator to the battery can be measured using a clamp-on digital multimeter set to read AC amperes.

## Slide 55: Figure 17–32 A mini clamp-on digital multimeter can be used to measure alternator output and unwanted AC current by switching the meter to read DC amperes.

## Slide 56: ALTERNATOR OUTPUT TEST (1 OF 2)
Connect the starting and charging test leads according to the manufacturer's instructions.
Turn the ignition on and observe the ammeter. It should be about 2 to 8 amperes.

## Slide 57: ALTERNATOR OUTPUT TEST (2 OF 2)
Start the engine and operate it at 2,000. Turn the load increase control slowly to obtain the highest reading on the ammeter scale while maintaining a battery voltage of at least 13 volts
Total the amperes from steps 2 and 3. Results should be within 10% (or 15 amperes) of the rated output.

## Slide 58: Figure 17–35 The output on this alternator is printed on a label.

## Slide 59: SUMMARY (1 OF 3)
Batteries can be tested with a voltmeter to determine the state of charge.
A battery drain test should be performed if the battery runs down.
Proper operation of the starter motor depends on the battery being at least 75% charged and the battery cables being of the correct size (gauge) and having no more than a 0.2 volt drop.

## Slide 60: SUMMARY (2 OF 3)
Charging system testing requires that the battery be at least 75% charged to be assured of accurate test results.
Cranking system voltage drop testing includes cranking the engine, measuring the drop in voltage from the battery to the starter, and measuring the drop in voltage from the negative terminal of the battery to the engine block.

## Slide 61: SUMMARY (3 OF 3)
The cranking circuit should be tested for proper amperage draw.
An open in the control circuit can prevent starter motor operation.
To check for excessive resistance in the wiring between the alternator and the battery, perform a voltage drop test.