## Slide 1: Automotive Electrical and Engine Performance
Eighth Edition
Chapter 01
Service Information, Tools, and Safety
Copyright © 2020, 2016 Pearson Education, Inc. All Rights Reserved

## Slide 2: Figure 1.1 The vehicle identification number (V I N) is visible through the base of the windshield and on a decal inside the driver’s door

## Slide 3: Figure 1.2 The vehicle emissions control information (V E C I) sticker is placed under the hood

## Slide 4: Figure 1.3 A typical calibration code sticker on the case of a controller. The information on the sticker is often needed when ordering parts or a replacement controller

## Slide 5: Figure 1.4 Casting numbers on major components can be either cast or stamped

## Slide 6: Figure 1.5 Electronic service information is available from aftermarket sources, such as ALLDATA and Mitchell On Demand, as well as, on websites hosted by vehicle manufacturers

## Slide 7: Figure 1.6 Technical service bulletins (T S B s) are issued by vehicle manufacturers when a fault occurs that affects many vehicles with the same problem. The T S B then provides the fix for the problem including any parts needed and detailed instructions

## Slide 8: Figure 1.7 The dimensions of a typical bolt showing where sizes are measured

## Slide 9: Figure 1.8 Thread pitch gauge used to measure the pitch of the thread. This bolt has 13 threads to the inch

## Slide 10: Figure 1.9 Bolts and screws have many different heads that determine what tool is needed

## Slide 11: Figure 1.10 The metric system specifies fasteners by diameter, length, and pitch

## Slide 12: Figure 1.11 Stronger threads are created by cold-rolling a heat-treated bolt blank instead of cutting the threads, using a die

## Slide 13: Figure 1.12 Metric bolt (cap screw) grade markings and approximate tensile strength

## Slide 14: Figure 1.13 Nuts come in a variety of styles, including locking (prevailing torque) types, such as the distorted thread and nylon insert type

## Slide 15: Figure 1.14 Washers come in a variety of styles, including flat and serrated used to help prevent a fastener from loosening

## Slide 16: Figure 1.15 A wrench after it has been forged but before the flashing, extra material around the wrench, has been removed

## Slide 17: Figure 1.16 A typical open-end wrench. The size is different on each end; notice that the head is angled 15 degrees at the end

## Slide 18: Figure 1.17 The end of a box-end wrench is angled 15 degrees to allow clearance for nearby objects or other fasteners

## Slide 19: Figure 1.18 A combination wrench has an open end at one end and a box end at the other end

## Slide 20: Figure 1.19 An adjustable wrench. Adjustable wrenches are sized by the overall length of the wrench and not by how far the jaws open. Common sizes of adjustable wrenches include 8, 10, and 12 inch

## Slide 21: Figure 1.20 The end of a typical line wrench, which shows that it is capable of grasping most of the head of the fitting

## Slide 22: Figure 1.21 A typical ratchet used to rotate a socket. A ratchet makes a ratcheting noise when it is being rotated in the opposite direction from loosening or tightening. A knob or lever on the ratchet allows the user to switch directions

## Slide 23: Figure 1.22 A typical flex handle used to rotate a socket, also called a breaker bar because it usually has a longer handle than a ratchet and, therefore, can be used to apply more torque to a fastener than a ratchet

## Slide 24: Figure 1.23 The most commonly used socket drive sizes include 1/4, 3/8, and 1/2 inch drive

## Slide 25: Figure 1.24 A 6-point socket fits the head of a bolt or nut on all sides. A 12-point socket can round off the head of a bolt or nut if a lot of force is applied

## Slide 26: Figure 1.25 Allows access to the nut that has a stud plus other locations needing great depth, such as spark plugs

## Slide 27: Figure 1.26 Using a clicker-type torque wrench to tighten connecting rod nuts on an engine

## Slide 28: Figure 1.27 A beam-type torque wrench that displays the torque reading on the face of the dial. The beam display is read as the beam deflects, which is in proportion to the amount of torque applied to the fastener

## Slide 29: Figure 1.28 Torque wrench calibration checker

## Slide 30: Figure 1.29 A flat-tip (straight-blade) screwdriver. The width of the blade should match the width of the slot in the fastener being loosened or tightened

## Slide 31: Figure 1.30 Two stubby screwdrivers that are used to access screws that have limited space above. A straight blade is on top and a #2 Phillips screwdriver is on the bottom

## Slide 32: Figure 1.31 A Torx bit and fastener

## Slide 33: Figure 1.32 An impact screwdriver used to remove slotted or Phillips head fasteners that cannot be broken loose using a standard screwdriver

## Slide 34: Figure 1.33 A typical ball-peen hammer

## Slide 35: Figure 1.34 A rubber mallet used to deliver a force to an object without harming the surface

## Slide 36: Figure 1.35 A dead-blow hammer that was left outside in freezing weather. The plastic covering was damaged, which destroyed this hammer. The lead shot is encased in the metal housing and then covered

## Slide 37: Figure 1.36 Typical slip-joint pliers are a common household pliers. The slip joint allows the jaws to be opened to two different settings

## Slide 38: Figure 1.37 Multigroove adjustable pliers are known by many names, including the trade name “Channel Locks®”

## Slide 39: Figure 1.38 Linesman’s pliers are very useful because it helps perform many automotive service jobs

## Slide 40: Figure 1.39 Diagonal-cut pliers are another common tool that has many names

## Slide 41: Figure 1.40 Needle-nose pliers are used where there is limited access to a wire or pin that needs to be installed or removed

## Slide 42: Figure 1.41 Locking pliers are best known by their trade name Vise Grips®

## Slide 43: Figure 1.42 Snap-ring pliers are also called lock ring pliers and most are designed to remove internal and external snap rings (lock rings)

## Slide 44: Figure 1.43 Files come in many different shapes and sizes. Never use a file without a handle

## Slide 45: Figure 1.44 Tin snips are used to cut thin sheets of metal or carpet

## Slide 46: Figure 1.45 A utility knife uses replaceable blades and is used to cut carpet and other materials

## Slide 47: Figure 1.46 A punch used to drive pins from assembled components. This type of punch is also called a pin punch

## Slide 48: Figure 1.47 Warning stamped on the side of a punch warning that goggles should be worn when using this tool. Always follow safety warnings

## Slide 49: Figure 1.48 Use a grinder or a file to remove the mushroom material on the end of a punch or chisel

## Slide 50: Figure 1.49 A typical hacksaw that is used to cut metal. If cutting sheet metal or thin objects, a blade with more teeth should be used

## Slide 51: Figure 1.50 A typical beginning technician tool set that includes the basic tools to get started

## Slide 52: Figure 1.51 A typical 40 inch wide top and bottom professional tool box

## Slide 53: Figure 1.52 A typical 12 volt test light

## Slide 54: Figure 1.53 Electric and butane-powered soldering guns used to make electrical repairs. Soldering guns are sold by the wattage rating. The higher the wattage, the greater the amount of heat created. Most solder guns used for automotive electrical work usually fall within the 60 to 160 watt range

## Slide 55: Figure 1.54 A battery-powered L E D trouble light

## Slide 56: Figure 1.55 A typical 1/2 inch drive air impact wrench. The direction of rotation can be changed to loosen or tighten a fastener

## Slide 57: Figure 1.56 A typical battery-powered 1/2 inch drive impact wrench

## Slide 58: Figure 1.57 A black impact socket. Always use an impact-type socket whenever using an impact wrench to avoid the possibility of shattering the socket, which could cause personal injury. If a socket is chrome plated, it is not to be used with an impact wrench

## Slide 59: Figure 1.58 An air ratchet is a very useful tool that allows fast removal and installation of fasteners, especially in areas that are difficult to reach or do not have room enough to move a hand ratchet or wrench

## Slide 60: Figure 1.59 This typical die grinder surface preparation kit includes the air-operated die grinder, as well as, a variety of sanding disks for smoothing surfaces or removing rust

## Slide 61: Figure 1.60 A typical pedestal grinder with a wire wheel on the left side and a stone wheel on the right side. Even though this machine is equipped with guards, safety glasses, or a face shield should always be worn whenever using a grinder or wire wheel

## Slide 62: Figure 1.61 Safety glasses should be worn at all times when working on or around any vehicle or servicing any components

## Slide 63: Figure 1.62 Steel-toed shoes are a worthwhile investment to help prevent foot injury due to falling objects. Even these well-worn shoes can protect the feet of this service technician

## Slide 64: Figure 1.63 One version of a bump cap is a molded plastic insert that is worn inside a regular cloth cap

## Slide 65: Figure 1.64 Protective gloves are available in several sizes and materials

## Slide 66: Figure 1.65 Remove all jewelry before performing service work on any vehicle

## Slide 67: Figure 1.66 Always connect an exhaust hose to the tailpipe of a vehicle to be run inside a building

## Slide 68: Figure 1.67 A binder clip being used to keep a fender cover from falling off

## Slide 69: Figure 1.68 Covering the interior as soon as the vehicle comes in for service helps improve customer satisfaction

## Slide 70: Figure 1.69 All oily shop cloths should be stored in a metal container equipped with a lid to help prevent spontaneous combustion

## Slide 71: Figure 1.70 Most newer vehicles have a triangle symbol indicating the recommended hoisting lift location

## Slide 72: Figure 1.71 (a) Tall safety stands can be used to provide additional support for the vehicle while on the hoist. (b) A block of wood should be used to avoid the possibility of doing damage to components supported by the stand

## Slide 73: Figure 1.72 This training vehicle fell from the hoist because the pads were not set correctly. No one was hurt but the vehicle was damaged

## Slide 74: Figure 1.73 (a) An assortment of hoist pad adapters that are often needed to safely hoist many pickup trucks, vans, and sport utility vehicles (S U V s). (b) A view from underneath a Chevrolet pickup truck showing how the pad extensions are used to attach the hoist lifting pad to contact the frame

## Slide 75: Figure 1.74 (a) The pad arm is just contacting the rocker panel of the vehicle. (b) The pad arm has dented the rocker panel on this vehicle because the pad was set too far inward underneath the vehicle

## Slide 76: Figure 1.75 (a) A hydraulic hand-operated floor jack. (b) Whenever a vehicle is raised off the ground, a safety stand should be placed under the frame, axle, or body to support the weight of the vehicle

## Slide 77: Figure 1.76 Drive-on-type ramps are dangerous to use. The wheels on the ground level must be chocked (blocked) to prevent accidental movement down the ramp

## Slide 78: Figure 1.77 Jumper cable usage guide. Follow the same connections if using a portable jump box

## Slide 79: Figure 1.78 The air pressure going to the nozzle should be reduced to 30 PSI or less to help prevent personal injury

## Slide 80: Figure 1.79 A typical fire extinguisher designed to be used on type A, B, or C fires

## Slide 81: Figure 1.80 A CO2 fire extinguisher being used on a fire set in an open drum during a demonstration at a fire training center

## Slide 82: Figure 1.81 A treated wool blanket is kept in an easy-to-open wall-mounted holder and should be placed in a central location in the shop

## Slide 83: Figure 1.82 A first aid box should be centrally located in the shop and kept stocked with the recommended supplies

## Slide 84: Figure 1.83 A typical eye wash station. Often a thorough flushing of the eyes with water is the first and often the best treatment in the event of eye contamination

## Slide 85: Figure 1.84 A warning label on a Honda hybrid warns that a person can be killed due to the high-voltage circuits under the cover

## Slide 86: Figure 1.85 The high-voltage disconnect switch is in the trunk area on a Toyota Prius. Insulated rubber lineman’s gloves should be worn when removing this plug

## Slide 87: Figure 1.86 The high-voltage shut-off switch on a Ford Escape hybrid. The switch is located under the carpet at the rear of the vehicle

## Slide 88: Figure 1.87 The shut-off switch on a G M parallel hybrid truck is green because this system uses 42 volts instead of higher, and possibly fatal, voltages used in other hybrid vehicles

## Slide 89: HOISTING THE VEHICLE 1

## Slide 90: HOISTING THE VEHICLE 2

## Slide 91: HOISTING THE VEHICLE 3

## Slide 92: HOISTING THE VEHICLE 4

## Slide 93: HOISTING THE VEHICLE 5

## Slide 94: HOISTING THE VEHICLE 6

## Slide 95: HOISTING THE VEHICLE 7

## Slide 96: HOISTING THE VEHICLE 8

## Slide 97: HOISTING THE VEHICLE 9

## Slide 98: HOISTING THE VEHICLE 10

## Slide 99: HOISTING THE VEHICLE 11

## Slide 100: HOISTING THE VEHICLE 12

## Slide 101: Copyright