Fuel Pump Testing

Meets ASE Task:  (A8-D-3) P-1  Inspect and test fuel pumps and pump control systems for pressure, regulation, and volume; perform necessary action.

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

_____  1.  Check service information and determine the factory specifications for acceptable fuel

pump pressure.

Fuel pump pressure specifications = ____________________________

_____  2.  Check service information, locate the fuel system pressure test valve or port, and

describe its location.

________________________________________________________________

_____  3.  Connect a fuel pressure gauge to the fuel pressure Schrader valve.

_____  4.  Start the engine and observe the fuel pressure.

fuel pressure = _________________

OK _____     NOT OK _____

_____  5.  Connect a hand-operated vacuum pump to the fuel

pressure regulator and apply 20 in. Hg. of vacuum.

Did the pressure decrease?  __________

_____  6.  Check fuel pump volume (0.5 to 1.0 gallons per

minute).

_____  7.  Based on this test, what is the necessary action?

________________________________________

________________________________________

________________________________________