Exhaust Gas Analysis

Meets ASE Task:  (A8-A-1) P-1  Prepare 4 or 5 gas analyzer; inspect and prepare vehicle for test, and obtain exhaust readings; interpret readings, and determine necessary action.

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

_____  1.  Check the instruction information for the exhaust gas analyzer being used to

determine the proper test procedures to follow.

__________________________________________________________________

__________________________________________________________________

_____  2.  Check the vehicle for exhaust leaks and other faults that could affect the exhaust gas

readings.

__________________________________________________________________

_____  3.  Prepare the vehicle for testing, which usually includes operating

the engine until normal operating temperature has been achieved.

List other items listed by the test equipment manufacturer that

should be performed.

__________________________________________

__________________________________________

_____  4.  Obtain the exhaust gas readings and compare them to specifications.

| Gas | Idle | 2500 RPM | General Specifications |
| --- | --- | --- | --- |
| HC |  |  | Max 50 PPM |
| CO |  |  | Max 0.5% |
| CO2 |  |  | 12% to 15% or higher |
| O2 |  |  | 0% to 2% |
| NOX |  |  | Less than 100 PPM @ idle Less than 1000 PPM @ wide open throttle |

_____  5.  Based on the exhaust gas readings, what is the necessary action?

__________________________________________________________________