Starter Voltage Drop/Current Draw Tests

Meets ASE Task:  (A6-C-1) P-1, (A6-C-2) P-1, and (A6-C-6) P-2  Perform starter current draw tests; determine necessary action.

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

_____  1.  Check service information for the specified starter current draw test procedure and

specifications.

__________________________________________________________________

__________________________________________________________________

NOTE:  Few vehicle manufacturers give starter current draw specifications with the starter installed on the vehicle.  Use the chart below as a guideline regarding the range of the maximum allowable starter draw.

4-cylinder engines = 150 to 185 amperes maximum (normally less than 100 A)

6-cylinder engines = 160 to 200 amperes maximum (normally less than 125 A)

8-cylinder engines = 185 to 250 amperes maximum (normally less than 150 A)

_____  2.  Perform the starter current draw test following the

manufacturer’s instructions.

Results:  ________ amperes

_____	3.  Connect the voltmeter, as shown in the

illustration, and crank the engine.  Observe the

voltmeter.

_____  4.  All test results should be less than 0.2 V (200 mV).

_____  5.  Based on the specifications and the test

results, what is the necessary action?

___________________________

___________________________

___________________________

___________________________