Charging Circuit Voltage Drop

Meets ASE Task:  (A6-D-5) P-1  Perform charging circuit voltage drop tests; determine necessary action.

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

_____  1.  Check service information for specified procedures and voltage drop specifications of

the charging circuit.

_____  2.  Connect one test lead of a digital multimeter set to read DC volts to the alternator

output terminal and the positive (+) terminal of the battery.

_____  3.  Start the engine and run to 2,000 RPM (fast idle).

_____  4.  Turn on the headlights to force the alternator to charge the battery.

_____  5.  The voltage drop reading should not exceed 0.40 volt.

_____ = the voltage drop of the insulated (power side) of the charging circuit

(between the output terminal of the alternator and the positive (+)

terminal of the battery).

OK_____   NOT OK_____

_____  6.  To test if the generator is properly grounded,

continue operating the engine at a fast

idle with the lights on, connect the meter

leads to the case of the generator and the

negative (-) terminal of the battery.  A reading

of greater than 0.20 volt indicates a

poor generator ground.

_____ = the voltage drop of the ground side

of the alternator (between the rear

housing of the alternator and the

negative (-) terminal of the battery).

OK_____   NOT OK_____

_____  7.  Based on the test results, what is the necessary action? _________________________

__________________________________________________________________