Ignition Scope Analysis

Meets ASE Task:  (A8-C-1) P-2 Inspect and test ignition primary and secondary circuit wiring and solid state components; test ignition coil(s); perform necessary action.

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

_____  1.  Check service information regarding the

specified method for attaching and using

a secondary circuit oscilloscope.

_______________________________

_______________________________

_____  2.  Type of ignition:

_____  Distributor

_____  Waste spark

_____  Coil-on-plug

_____  3.  Connect the ignition scope to the system as per the scope manufacturer’s

instructions.

_____  4.  Brand of scope used:  ________________________________________

_____  5.  Describe the hookup procedure. ___________________________________________

_____  6.  Start the engine and observe the secondary ignition waveform.

Firing Voltage (KV)			Spark Line Length (ms)

(voltage should be 5-15 KV)	            (length should be 1-2 ms)

Cylinder #1          _______________________		_____________________

Cylinder #2          _______________________		_____________________

Cylinder #3          _______________________		_____________________

Cylinder #4          _______________________		_____________________

Cylinder #5          _______________________		_____________________

Cylinder #6          _______________________		_____________________

Cylinder #7          _______________________		_____________________

Cylinder #8          _______________________		_____________________

_____  7.  Based on the test results, what is the necessary action? _________________________