Primary Ignition Inspection and Testing

Meets ASE Task:  (A8-C-2) P-1  Inspect, test, and/or replace ignition control module, powertrain/engine control module; reprogram as necessary.

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

_____  1.  Check service information and determine what type of

ignition system is used on this vehicle?

_____  Distributor ignition (DI)

_____  Waste-spark (EI)

_____  Coil-on-plug

_____  Other (describe) _______________________

_____  2.  Check service information and determine what type of

primary circuit switching device is used on this system.

_____  Pickup coil (pulse generator)  Used on most

distributor-type ignition systems.

_____  Hall-effect sensor

_____  Magnetic sensor

_____  Optical sensor

_____  Other (describe) _______________________

_____  3.  Check service information and determine what color wires are used on the switching

device?

_______________, _______________, _______________, _______________

_____  4.  The primary ignition switching device signal goes to the:

_____  Ignition control module (ICM)

_____  Computer (PCM)

_____  Other (describe) _____________________________________________

_____  5.  Using the service information, what are the steps to diagnosis a no-spark condition?

______________________________________________________

______________________________________________________

______________________________________________________

_____  6.  Could a fault in the primary ignition sensor cause a no-spark condition?

Yes _____     No _____

_____  7.  Based on inspection and tests, what is the necessary action? ____________________