MAP Sensor Diagnosis

Meets ASE Task:  (A8-B-7) P-2  Inspect and test sensors, actuators, and circuits using a graphing multimeter (GMM)/digital storage oscilloscope (DSO); perform necessary action.

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

_____  1.  Check service information for the specified MAP sensor diagnosis procedure.

__________________________________________________________________

_____  2.  Perform a thorough visual inspection including:

a.   Check the condition of vacuum hose (if equipped).

b.   Check that the vacuum hose routing does not have any dips or sags in the

vacuum hose between the sensor and the intake manifold.

NOTE:  A dip or low portion in the vacuum hose can create a trap where liquid fuel

(condensed gasoline fumes) or water (condensed steam) can accumulate and block the

vacuum signal to the MAP sensor.

c.   Disconnect the vacuum hose (if equipped) from the MAP sensor.  If anything

such as a liquid or other substance comes out of the sensor or the hose, replace

the MAP sensor.  Reconnect the vacuum hose to the MAP.

_____  3.  Turn the ignition key on (engine off), read and record the MAP sensor voltage (or

frequency) = _____ volts (Hz) (use either a scan tool or digital meter connected to the

signal wire).  (Should be about 4.60 to 4.80 volts or 156-159 Hz.)

OK _____    NOT OK _____

_____  4.  Start the engine and operate until normal operating temperature is achieved.  Read and

record the MAP sensor voltage (or Hz) at idle speed = ________volts (Hz).  (Should

be between 0.9 and 1.6 volts (102-109 Hz) if the engine varies between 17 and 21

inches of Hg.)     OK _____  NOT OK _____

_____  5 .  Based on these tests, what is the necessary action?

__________________________________________

__________________________________________

__________________________________________