Throttle Position Sensor Scan Tool Diagnosis

Meets NATEF Task:  (A8-B-7) Inspect and test sensors, actuators, and circuits using a graphing multimeter (GMM)/digital storage oscilloscope (DSO); perform necessary action.  (P-2)

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

_____  1.  Check service information for the specified testing procedures and specifications for

the throttle position (TP) sensor.

Recommended testing procedure: ______________________________________

Throttle position sensor specification: ___________________________________

_____  2.  Connect a scan tool to the data link connector (DLC).  Check and record any throttle

position-related diagnostic trouble codes (DTCs).

DTC					Description of DTC

________________________	____________________________________

________________________	____________________________________

________________________	____________________________________

_____  3.  With the ignition on, engine off (KOEO), connect a scan tool and check the output of

the TP sensor at:

Idle = ________      ½ throttle = ________      Wide open (WOT) = ________

_____  4.  Based on the test results, what is the necessary action?

______________________________

______________________________

______________________________

______________________________