Oxygen Sensor Voltmeter Diagnosis

Meets NATEF Task:  (A8-B-7) Inspect and test sensors, actuators, and circuits using a graphing multimeter (GMM)/digital storage oscilloscope (DSO); perform necessary action.  (P-2)

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

_____  1.  Locate the oxygen sensor(s) and carefully back probe the sensor wire at a connector

with a “T” pin.

_____  2.  Set the digital multimeter to read DC

volts (DCV).

_____  3.  Attach the red lead of the digital voltmeter

to the sensor and ground the black meter

lead to a good clean non-painted ground.

_____  4.  Start the engine and allow it to run at 2500

RPM for 2 minutes to get the oxygen sensor

up to operating temperature and get the engine into closed loop.

_____  5.  Select MIN/MAX record and maintain the engine speed at 2500 RPM for 2 additional

minutes.

Record the    MIN ______      MAX ______    AVERAGE ______

_____  6.  Results:  MIN should be below 200 mV and MAX should be above 800 mV.

The average should be about 450 mV.

a.  If the average is higher than 450 mV, the engine is operating with a rich air-

fuel mixture.

b.  If the average is lower than 450 mV, the engine is operating with a lean air-

fuel mixture.

_____  7.  Based on the test results, what is the necessary action? _________________________

__________________________________________________________________