Oxygen Sensor Scope Diagnosis

Meets NATEF Task:  (A8-B-7) Inspect and test sensors, actuators, and circuits using a graphing multimeter (GMM)/digital storage oscilloscope (DSO); perform necessary action.  (P-2)

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

_____  1.  Locate the oxygen sensor(s) and carefully back probe the sensor wire at a connector

with a “T” pin.

_____  2.  Set the scope to 1s/div time base and 200 mV/div for the volts per division setting.

_____  3.  Attach the scope probe to the oxygen sensor signal wire.  Connect the ground wire

from the scope probe to a good engine ground.

_____  4.  Start the engine and allow it to run at 2500 RPM for 2 minutes to allow the oxygen

sensor to reach operating temperature and the engine to achieve closed loop operation.

_____  5.  Select the proper time base and volts per division

(try 200 mS per division and 200 mV per division).

_____  6.  Observe the scope pattern:

a.   What is the highest voltage observed?

______ Max. volts

b.   What is the lowest voltage observed?

______ Min volts

c.   How many times does the voltage cycle in one second?  ______

(Should  be 0.5 to 5.0 Hz.)

OK ________      NOT OK ________

_____  7.  Based on the results of the test, what is the necessary action?  ___________________

_________________________________________________________________