Injector Current Ramping

Meets NATEF Task:  (A8-D-7)  Inspect and test fuel injectors.  (P-2)

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

_____  1.  Check service information for the type of fuel injector being used.

____  Saturated

____  Peak and hold

_____  2.  Connect a digital storage oscilloscope (DSO) or graphing multimeter (GMM) to the

pulsed side of the injector.  (Check service information for the color of wire used for

the pulse.)

_____  3.  Start the engine and observe the current waveform.

_____  4.  Does the current waveform correct?     _____  Yes     _____  No

_____  5.  What is the injector pulse-width? __________ (normally between 1.5 and 3.5 ms at

idle on a warm engine)

_____  6.  Based on the test performed, what is the necessary action?  _____________________

_________________________________________________________________