Ford Pressure Feedback EGR (PFE)

Meets NATEF Task:  (A8-E-6)  Inspect, test, service and replace components of the EGR system, including EGR tubing, exhaust passages, etc.; perform necessary action.  (P-2)

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

Exhaust back pressure is used to control the amount of exhaust gas recirculation (EGR).  The EGR valve is normally closed at both idle and wide open throttle (WOT).  The EGR vacuum regulator (EVR) solenoid is pulsed on and off to give the ideal amount of EGR flow for a given back pressure.

| Back Pressure | Voltage |
| --- | --- |
| 0 psi | 3.25 |
| 0.5 psi | 3.66 |
| 0.75 psi | 3.78 |
| 1.0 psi | 4.08 |
| 1.25 psi | 4.28 |
| 1.50 psi | 4.50 |
| 1.80 psi | 4.75 |

_____  1.  Check service information for the specified procedures for testing the Ford pressure

feedback EGR.

__________________________________________________________________

__________________________________________________________________

_____  2.  Voltage at idle = _________ volts (should be 3.25 V)

OK _____    NOT OK _____

_____  3.  Voltage at steady speed (50 mph) = _______ volts (should be 3.4 to 3.8 V).

# OK _____    NOT OK _____

_____  4.  Based on the test results, what is the necessary

action?

__________________________________