Evidence of Previous Repairs

Meets NATEF Task:  (A8-A-2)  Identify and interpret engine performance concern; determine necessary action. (P-1)

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

_____  1.  Check for a recent oil change.

a.  The incorrect viscosity of oil could have been

installed.

b.  The incorrect oil filter could have been installed.

_____  2.  Check for recent body work.

a.   Ground wires could be left disconnected, loose or

attached to a painted (insulated) surface.

b.   Windshield replacement could cause water leaks

to get into computers or wiring.

c.   Electrical connectors could be disconnected.

d.   Wiring could have been spliced or repaired - look

for improper repair procedure that could lead to

corrosion or high electrical resistance.

_____  3.  Check for recent clutch or transmission repairs.

a.   Collapsed mounts can cause vibration.

b.   A dislocated cradle can cause pulling to one side.

c.   Many ground wires may have been left unattached.

_____  4.  Recent filter changes or PCV valve replacement.

The probability of the incorrect part number being installed can cause driveability

problems.

OK _____    NOT OK _____