Engine Operating Temperature

Meets NATEF Task:  (A8-A-10)   Verify engine operating temperature; determine necessary action.  (P-1)

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

_____  1.  Check service information for the specified thermostat rating and normal operating

temperature range.

Thermostat temperature _______________

Normal operating temperature ______________

_____  2.  Start the engine and operate until normal operating temperature is achieved and the

thermostat is fully open.

_____  3.  Using an infrared pyrometer, measure the radiator at the inlet, middle, and outlet

sections and record the readings.

Inlet 	=  __________ (should be the hottest)

Middle =  __________ (should be cooler than the inlet section)

Outlet  =  __________ (should be cooler than the middle)

OK _____	NOT OK _____

_____  4.  Aim the infrared pyrometer to all sections of the radiator and look for any areas that

are cooler than the surroundings which indicate a restricted or clogged portion of the

radiator.

OK _____	NOT OK _____

_____  5.  Check engine coolant temperature (ECT) sensor valve, using a scan tool:  __________

_____  6.  Based on the inspection and temperature tests, what is the necessary action?

__________________________________________________________________

__________________________________________________________________