Engine Cooling System Inspection

Meets NATEF Task:  (A8-A-10)   Perform cooling system pressure test; perform necessary action. (P-1)

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

_____  1.  Inspect the radiator for exterior leaks or clogged

areas due to bugs, dirt, or debris, and clean as

required.

OK _____	NOT OK _____

_____  2.  Pressure test the cooling system.  The entire

system should hold about 15 psi for 5

minutes, unless there is a leak.

OK _____	NOT OK _____

Location of leak ____________________

_____  3.  Pressure test the radiator cap.  The cap holds _________ psi.

OK _____	NOT OK _____

_____  4.  Check the freezing point of the coolant using an hydrometer = __________

[should be -34( F (-37( C) or lower].

OK _____	NOT OK _____

_____  5.  Check the boiling point of the coolant using an hydrometer = __________.

OK _____	NOT OK _____

_____  6.  Based on the results of the testing, what is the necessary action? _______________

_______________________________________________________________