Fluids Check

Meets NATEF Task:  (A8-A-4)  Inspect engine assembly for fuel, oil, coolant, and other leaks; determine necessary action.  (P-2)

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

_____  1.  Check the air filter using a light bulb.

_____  2.  Check the engine oil level and condition.

Level:  ____low     ____okay     ____overfilled

Color:  ____black   ____dark brown     ____amber

_____  3.  Check the brake fluid (1/4" from the top).

_____  4.  Check all hoses (check for cracks, swollen, brittle, or

leaking hose).

_____  5.  Check the battery water (if possible).

_____  6.  Clean the battery and tighten all connections.

_____  7.  Check the power steering fluid (use power steering fluid only unless otherwise

specified).

_____  8.  Check the radiator coolant level (check when cold only!).  The coolant should be

within 3" of the top of the filler neck.  (The reserve tank should be filled to the

indicated mark with a 50/50 mixture of antifreeze and water.)

_____  9.  Check the windshield washer fluid.

_____ 10. Check the automatic transmission fluid with the engine running at idle, the vehicle on

level ground, the transmission in neutral (or park) and the transmission hot.  If the

level of the fluid is not between "add and full", add the specified ATF as

required.

NOTE:  The add mark means - add 1 pint (1/2 quart).

_____ 11. Based on the tests and inspection performed, what is the necessary action? _________

__________________________________________________________________